Subsea compression

Subsea compression in this project consists of two consecutive compression periods; constant field rate (plateau rate of 106  Sm3/D) followed by constant compressor pressure increment of 32 bara with flow rate decline .  In both periods the wells will operate with fully open choke.

- Stage: constant field rate

  - Field rate is constant

  - Compressor discharge pressure is constant

  - Suction pressure of compressor is changing with recovery.

  - Excel solver is need to calculate the rate produced by each template

  - End of this stage is reached  when compressor pressure increment reaches 32 bara

- Stage: constant  compressor pressure increment

- Compressor pressure increment maintained constant (32 bara)

- The total field production rate is declining (smaller rate at each time step)

- The rate contribution of each template is needed to be calculated using Solver.

- The discharge pressure of the compressor is changing at each time-step