## Slide 1
ROSE meeting
24th - 27th April 2017
Trondheim, Norway
Impact of stress and saturation on seismic dispersion in shales - Laboratory measurements
by
Dawid Szewczyk, Rune M. Holt, Andreas Bauer

## Slide 2
Internal load cell
Low-frequency unit consisting of piezoelectric actuator and piezoelectric force sensor, ε
Endcap with ultrasonic transducers (Vp, Vs) and pore-fluid line
Rock sample (1" diameter) with 8 strain gages (4 axial, 4 radial) glued to it (rubber sleeve was removed)
Endcap with ultrasonic transducers (Vp, Vs) and pore-fluid line
LVDT
Compaction cell for seismic-dispersion measurements
Compaction tests
Control of confining stress, axial stress, and pore pressure
Ultrasonic velocities, vP, vS
Dynamic stiffness (Young's modulus, Poissons's ratio) at seismic frequencies (0.1 – 150 Hz)

## Slide 3
Sample preparation
Samples were stabilized in desiccators with different relative humidity [RH]
11.3% [LiCl]
32.9% [MgCl]
54,7% [Mg(NO3)2]
75.4% [NaCl]
Mancos shale: outcrop material preserved in oil, gas shale, ρ  2.57 g/cm3, 7% porosity,  24% clay,  43% quartz,  20% carbonates,  1% -1,5% TOC
Pierre shale: outcrop material preserved in oil, ρ  2.40 g/cm3,  16% porosity,  48% clay,  27% quartz,  6% carbonates
RH → saturation conversion: mineral density + XRD composition → ρT (0 porosity);
ρT + ρM(measured) → sample porosity; φ + VS→ Vφ; Vφ + ΔM → SW
0o
45o
90o
Mancos shale
0o
45o
90o
Pierre shale

## Slide 4
Data processing
Seismic frequencies → Young's modulus and Poisson's ratio (E, )
Ultrasonic frequencies → P- and S-wave velocities
Conversion
Isotropic materials
(sandstones):
TI medium (shales):
ρρρ
0o
45o
90o
Measurements for all three orientations:
Mancos shale – 0.11 Sw and as-received
Pierre shale – 0.1 and 0.48 Sw
For the other saturation states, the Thomsen anisotropy parameters were extrapolated.

## Slide 5
Quality check
TI symmetry requires:
0
90
EV, VH
EH, HV, HH
Young's moduli and Poisson's ratios obtained with 0o, 45o, and 90o-oriented samples are consistent with TI symmetry
Pierre Sw=0.1
Pierre Sw=0.1

## Slide 6
Stress dependence – VPV
Stress sensitivity → clear difference between seismic and ultrasonic frequencies
( ̴ twofold higher at seismic regime)
Dispersion → ̴ 23% in VPV between 1 Hz and 500 kHz
Dispersion decreases with increasing stress
Frequency (Hz) | Stress sensitivity (m/s/MPa)
1 | 7.45
21 | 7.38
105 | 7.29
500 k | 3.7
Mancos as-received

## Slide 7
Stress dependence – VPV
Frequency (Hz) | Stress sensitivity (m/s/MPa)
1 | 18.37
500 k | 14.30
SW=0.10
Frequency (Hz) | Stress sensitivity (m/s/MPa)
1 | 14.76
500 k | 12.60
SW=0.23
Frequency (Hz) | Stress sensitivity (m/s/MPa)
1 | 15.28
500 k | 14.95
SW=0.48
Frequency (Hz) | Stress sensitivity (m/s/MPa)
1 | 7.95
500 k | 12.48
SW=0.70
Stress sensitivity → different for seismic and ultrasonic and saturation dependent
Dispersion → ̴ 10% in VPV between 1 Hz and 500 kHz (SW=0.12) and saturation dependent
Dispersion decreases with increasing stress (beside SW=0.72)
Effects of saturation increase → stress sensitivity decreases, dispersion increases
Pierre Sw=0.1
Pierre Sw=0.23
Pierre Sw=0.48
Pierre Sw=0.70

## Slide 8
Saturation dependence – EV,νVH
Increase in RH (water saturation) results in:
Gradual decrease in Young's modulus at seismic frequencies +
Increase of Young's-modulus dispersion →
Complex behavior of Young's modulus at ultrasonic frequencies
Saturation | Seismic frequencies | Ultrasonic frequencies
<0.3 |  | 
0.3-0.7 |  | 
>0.7 |  | 
velocity dispersion strongly increases between Sw > 0.3 and Sw < 0.7

## Slide 9
What is causing the observed softening and dispersion effects?
Relative humidity (RH) is directly related to the total suction st.
In sedimentary rocks, the pore fluid and physicochemical interactions have a strong
impact on the petrophysical rock properties.
)
gas constant
temperature
molar volume
The total suction consists of two components, matric suction (solid phase) and solute
suction (solute concentration in the pore fluid).
Mechanisms generating matric suction
Capillary
Osmotic
Electrostatic
(adsorption)
Increased RH influence adsorption → gradual reduction of grain-surface energy
(affecting the rock stiffness) and increase in water-layer thickness (Murphy et al., 1984).

## Slide 10
What is causing the observed softening and dispersion effects?
Water adsorption at grain contacts can also explain the observed increase in dispersion with increased water content. Displacement of water molecules during stress variation (an increase in stress results in an increase of the chemical potential of the water in between the grains, making it energetically more favorable for the water to move away from the grain contact) takes time due to viscous forces - local flow type mechanism.
Smaller grain-surface energy →
reduced stiffness (e.g. Clark et al., 1980;
Murphy et al., 1984)

## Slide 11
Modelling of the fluid-saturation effects
Anisotropic Gassmann + effective rock-frame modulus and the pore-fluid modulus
accounting for rock-fluid interaction effects such as adsorption effects or dispersion.
Pore-fluid modulus → Brie’s mixing
Rock-frame modulus → additional parameter (independent for Pierre shale and
Mancos shale) linearly relating frame modulus and saturation.
Mancos shale
Pierre shale

## Slide 12
Summary
Stress dependence of P-wave velocities can be significantly different at seismic and ultrasonic frequencies (needs to be accounted for when stress sensitivities are obtained at ultrasonic frequencies and applied to the interpretation of 4D seismic data).
Increase in water saturation causes increase in EV dispersion and softening of the shale at seismic frequencies leading to complex EV behaviour at ultrasonic frequencies.
Mancos and Pierre shale exhibit qualitatively similar saturation effects on dynamic stiffness, acoustic velocities, and velocity dispersion.
Adsorption may be the dominant mechanism in the rock physics of partially saturated shales but other effects (capillarity; osmotic suction; desiccation-induced porosity changes, etc.) may have an impact as well → more studies needed.

## Slide 13
Summary
The authors would like to acknowledge support from:
BIGCCS Centre funded by the Norwegian Research Council, ConocoPhillips, Engie, Gassco, Shell, Statoil, and Total
KPN project on "Shale Rock Physics for Increased Recovery" funded by the Norwegian Research Council, BP, DONG, Engie, Mærsk, and Total
Acknowledgements