## Slide 1: Estimating S-wave velocities and changes from tube waves
Daniel Wehner
Filipe Borges, Izzie Y. Liu, Martin Landrø
Department of Geoscience and Petroleum, NTNU Trondheim
ROSE 2018

## Slide 2
Tube wave history
  Lamb (1898), Biot (1952), Somers (1953), …
Generated at interfaces striking the borehole (Hardage, 1981)
Usage:
  identification of fractures (Hornby et al. 1989; Li et al., 1994)
  permeability of formation when coupled to borehole fluid (White, 1965; Chang et al., 1988; Winkler et al. 1989)
  estimate S-wave of formation from acoustic logging (Stevens and Day, 1986)
  often considered as noise in VSP
casing
fluid
geological formation
Borehole
tube wave
Tube Wave

## Slide 3
Is it possible to estimate the Shear Modulus and S-Wave velocity
changes in the geological formation by measuring Tube waves?
Advantages
  Fixed source position
    position and firing time is not required
  Only hydrophones are required
    free from mechanical noise (Peng, 1996)
    low-cost
  Permanently installed system
  Might use passive seismic recordings
Problems
  Precise estimation of tube wave velocity
  Tube wave depends on several borehole parameter (casing, logging tool, borehole fluid)
Motivation

## Slide 4: Theory

## Slide 5
rmin
rmax
dcas
fluid
tool
casing
geological formation
Important parameter for Tube wave vs. Shear Modulus of formation
Theory

## Slide 6
(2) Only casing:
(Marzetta and Schoenberg, 1985, Norris 1990)
(3) Logging tool and casing:
(Norris, 1990)
(1) Only logging tool:
(Marzetta and Schoenberg, 1985)
rmin
rmax
fluid
tool
dcas
fluid
rmin
rmax
fluid
tool
dcas
Theory

## Slide 7
(1) Only logging tool:
(2) Only casing:
(3) Logging tool and casing:
rmin
rmax
fluid
tool
dcas
dcas
fluid
rmin
rmax
fluid
tool
Theory

## Slide 8
Casing thickness
Borehole diameter
……
reference
decreasing
increasing
rmin
rmax
dcas
Sensitivity to different parameter

## Slide 9: Experiments

## Slide 10
Source
Workhall
1.25 m
H24
1.50 m
water table
Graben
Well 1
(depth: 30 m)
Source
0.15 m
Well 2
(depth 95 m)
0.15 m
Source
1.6 m
H24
2.60 m
water table
Experiments
Wells

## Slide 11
1.25 m
H24
1.50 m
water table
Graben
Well 1
(depth: 30 m)
Source
0.15 m
Well 2
(depth 95 m)
0.15 m
Source
1.6 m
H24
2.60 m
water table
Experiments
Receiver: 24 channel hydrophone array
  spacing: 1 m
  frequency range1 Hz – 10000 Hz
Tests:
  Well 1: September 17, October 17 and March 18
  Well 2: October 17
Well 1:
  diameter: 15 cm
  casing thickness: 4 mm
Well 2:
  diameter: 30 cm
  casing thickness: 5 mm

## Slide 12: Results

## Slide 13
Recordings
Well 2 (95 m)
Well 1 (30 m)
Down- and upgoing Tube Wave
Down- and upgoing Tube Wave
bandpass filter: 50 Hz – 450 Hz

## Slide 14
Recordings
Passive recordings
Peaks at
  Shallow well = 20 Hz
  Deep well = 6 Hz
Active recordings and noise
> 30 Hz: signal above noise level

## Slide 15
Tube Wave Velocity
upgoing tube wave
downgoing tube wave
casing wave
Least-squares line fit to estimate velocity
between 50-450 Hz
dispersion effect: velocity decrease < 0.02 % between 0-1000 Hz
Well 2 (95 m)
Well 1 (30 m)

## Slide 16
Tube Wave Velocity
September 17
October 17
March 18
October 17
High accuracy in results
Well 2 (95 m)
Well 1 (30 m)
could be caused by temperature difference in borehole fluid
(1oC  2 m/s)

## Slide 17
Estimated Formation Properties
S-wave velocity
Shear modulus
Smaller estimated range in well 2
higher accuracy of tube wave velocity
different borehole geometry
( = 2000 kg/)

## Slide 18: Field example

## Slide 19
Precipitation of salt
(Lab examples: Vanorio et al., 2011; Grude et al. 2014)
Field example: CO2 injection
Changes due to CO2 injection
Pore pressure Pp increase
(Field examples: Duffaut and Landrø, 2007; Grude et al. 2014)
sandstone, initial porosity = 0.3
salinity: 50000 ppm
inital Pp = 7.5 MPa (ca. 750 m depth)
Hertz-Mindlin model

## Slide 20
Field example: CO2 injection
t1: injection starts
t2: injection stops
t3: initial pore pressure is reached
Time steps during CO2 injection
36.5 cm (13 in.)
1 cm (0.38 in.)
14 cm (5 in.)
inital Pp = 7.5 MPa (ca. 750 m depth)
decrease of 2.5 MPa due to injection

## Slide 21
Absolute estimation of shear modulus/S-wave is diffucult
  additional measurements required
Monitoring could be feasible
  temperature in borefluid should be measured
  high accuracy of measured tube wave velocity required
Feasiblity depends on geological setting and borehole set-up
  borehole should have: thin casing, large diameter, small casing shear modulus
  geological formation with low initial shear modulus
Advantages
  no firing time and source location required (Passive Seismics?)
  hydrophones: cheap, permanent monitoring system (Fibre Optics?)
Disadvantages
  tube wave depends on several parameter
Conclusion/Discussion

## Slide 22
The WAVES project, funded by the European Union’s Horizon 2020 research and innovation programme under the Marie Slodowska-Curie grant agreement.
Norwegian University of Science and Technology Trondheim

## Slide 23
Biot, M. A. [1952] Propagation of elastic waves in a cylindrical bore containing a fluid. Journal of Applied Physics, 13, 997-1005.
Duffaut, K. and Landrø, M. [2007] Vp/Vs ratio versus differential stress and rock consolidation – A comparison between rock models and time-lapse AVO data. Geophysics, 72 (5), C81-C94.
Grude, S., Landrø, M. and Dvorkin, J. [2014] Pressure effects caused by CO2 injection in the Tubåen Fm., the Snøhvit field. International Journal of Greenhouse Gas Control, 27, 178-187.
Lamb, H. [1898] On the velocity of sand in a tube as affected by the elasticity of the wall. Manchester Memoires, 42, 1-16.
Marzetta, T. L. and Schoenberg, M. [1985] Tube waves in cased boreholes. SEG Technical Program Expanded Abstract, 34-36.
Norris, A. N. [1990] The speed of a tube wave. Journal of Acoustical Society of America, 87, 414-417.
Peng, C., Lee, J. M. and Toksöz, M. N. [1996] Pressure in a fluid-filled borehole caused by a seismic source in stratified media. Geophysics, 61, 43-55.
Somers, E. [1953] Propagation of acoustic waves in a liquid-filled cylindrical hole surrounded by an elastic solid. Journal of Applied Physics, 24, 513-521.
Vanorio, T., Nur, A. and Ebert, Y. [2011]. Rock physics analysis and time-lapse rock imaging of geochemical effects due to the injection of CO2 into reservoir rocks. Geophysics, 76 (5), O23-O33.
References

## Slide 24: Appendix

## Slide 25
Estimated Formation Properties
S-wave velocity
Long and Donohue, 2007
‘’Reference‘’ test site Edberg
location of well2
additional test site (Edberg)
at Edberg site ca. 300 m/s
(down to 10 m depth)
at wells ca. 450 m/s
(down to 26 m depth)
( = 2000 kg/)
500 m

## Slide 26
Theory
  Relation between Tube wave and S-wave in the surrounding formation
Experiments
  Set up and parameter
Results
  Measured Tube wave
  Estimation of S-wave in the surrounding formation
Discussion
  Sensitivity analysis
  Theoretical field example
Conclusion
Outline

## Slide 27
Recordings
Well 2 (95 m)
Well 1 (30 m)
Down- and upgoing Tube Wave
bandpass filter: 50 Hz – 450 Hz

## Slide 28
Recordings
Well 2 (95 m)
Well 1 (30 m)
Single receiver (Nr.: 20)
Well 1 (30 m)
Well 2 (95 m)
Well 1 - Well 2
repeatability of 80 hammer shots
longer repeatable signal in deep well

## Slide 29
Recordings
Passive recordings
Peaks at
  Shallow well = 20 Hz
  Deep well = 6 Hz

## Slide 30
Casing thickness
Tool thickness
Borehole thickness
Bulk Modulus: borehole fluid
……
experimental result
decreasing
increasing
increasing
decreasing
rmin
rmax
dcas
Sensitivity to different parameter

## Slide 31
Geometry
Fluid  Water
Casing  Steel
Logging tool  Keflar
rmin
rmax
dcas
fluid
tool
casing
geological formation
Paramter

## Slide 32
Recorded data:
  stacked
  f-k filtered
Model:
  tube wave starts at borehole head
  different velocities, reflection coefficients at bottom, no attenuation
,
,
,
,
Measured and Modelled Data

## Slide 33
Velocity of the tube wave is influenced by (Galperin, 1985)
  the borehole casing
  elastic constants of surrounding formation
  elastic constants of drilling fluid
  the logging tool
Intensity of the tube wave is influenced by (Galperin, 1985)
  contact between casing and formation, e.g. cementation - better coupling  higher intensity
  density of the fluid - lower density  lower intensity
  depth below water level - increasing depth  lower intensity
  for Geophones: applied force for clamping the tool - higher force  lower intensity
Tube Wave dependency

## Slide 34
In soil
Boussinesq’s formula
Boussinesq stress coefficient:
r = offset
Force at surface:
Vs change due to loading

## Slide 35
In rocks
assuming
, ,
Force at surface:
Vs change due to loading

## Slide 36
In rocks
Modified guess of Boussinesq’s formula
Force at surface:
Vs change due to loading

## Slide 37: 1. Holding construction of hydrophone array
holding board: ‘’seals’’ the well and more energy is kept inside the borehole (test 3)
holding metal frame: nearly open to the top of the borehole (test 2)

## Slide 38: 2. Position of water table in well
Floor of work hall
Floor of graben
2 m
H24
2.6 m
water surface
1.8 m
95 m deep well
Floor of work hall
Floor of graben
2 m
1.15 m
H24
1.45 m
water surface
1.25 m
different interaction of first downgoing tube wave and ghost reflection in shallow and deep well
35 m shallow well

## Slide 39: 3. Variation of water table position
Floor of work hall
Floor of graben
2 m
1.15 m
H24
1.45 m
water surface
1.25 m
Floor of work hall
Floor of graben
2 m
1.85 m
H24
0.90 m
water surface
1.25 m
Effective pressure change of 0.01 Mpa
= difference in water table
max. 0.1 % velocity change (1.2 m/s in )
(Hertz-Mindlin)
Effective pressure change of 0.01 Mpa
= difference in water table
different for near surface soils/unconsolidated rocks???

## Slide 40: 4. Radial position of hydrophone array
centered
not centered
change of wave form, interference with other waves for different hydrophone positions  impact on velocity estimation in fk-domain
should not cause a change of the tube wave velocity (Norris, 1990)
Test 5: not centered
Test 6,7 : centered

## Slide 41: 5. Temperature effect
water surface
1.85 m
H24
0.90 m
1.25 m
depth: 0 m
Deep well: 22.11.2016

## Slide 42: 5. Temperature effect
Dixon, 2007:

## Slide 43: 6. Interaction with second well/near field effect
Tool installed in deep well
Floor of work hall
Floor of graben
2 m
H24
2.6 m
water surface
1.8 m
95 m deep well
Floor of work hall
Floor of graben
2 m
H24
2.6 m
water surface
1.8 m
95 m deep well
hydrophones in deep well also show upgoing waves earlier than first bottom reflection
  is recoridng in deep well inpmacted by shallow well and vice versa?

## Slide 44: 6. Interaction with second well
Frequencies between 50 – 450 Hz are used
test 1
test 2
1224.5 ± 3.3 m/s
1225.7 ± 4.2 m/s

## Slide 45: 7. Background noise (surface waves)