## Slide 1: Nan Cheng, Statoil 26-June-2013
Integration of 4D Seismic & Production Data for Reservoir Management – Application to Norne
26-27 June 2013, Trondheim, Norway
Introduction to Norne Oil Field

## Slide 2: Norne & Its Satellite Fields
Norne Production Licence 128 Production start Norne: Nov. 1997
Urd Production Licence 128 Production start Urd: 2005
Alve Production Licence 159 Production start Alve: 2009
Water depth 380 m
Statoil is operator
Production end 2021 (FPSO lifetime)
Company | Norne | Urd | Alve
Petoro as | 54% | 24,5% | 
Statoil ASA | 39,1% | 64 % | 85%
Eni Norge as | 6,9% | 11,5% | 
DONG E&P Norge |  |  | 15%
200 km to Norwegian coast
80 km to Heidrun Field

## Slide 3: High Quality Reservoir
Consisting of 4 segments
Good quality sands in Not, Ile, Tofte, and Tofte formations
Porosity of 24 - 28 %, k = 100 - 3000 mD
140 m HC column (110m oil and an overlying gas cap)
Initial Pres = 273 bar @ 2639 m TVD, Tres= 98 °C
Pb = 250 bara, GOR= 111 Sm3/Sm3
Oil SG = 0.7, Oil viscocity = 0.5 cp
Boi=1.32 Rm3/Sm3
Rock wettabiliy: mixed
C
D
E
G

## Slide 4
NORNE 2006 | 
Not 3 | Upper Not Shale
Not 2 (Not sandstone) | Not 2.3
 | Not 2.2
 | Not 2.1
Not 1 | Lower Not Shale
Ile 2 | Ile 2.2
 | Ile 2.1
Ile 1 | Ile 1.3
 | Ile 1.2
 | Ile 1.1
Tofte 2 | Tofte 2.2
 | Tofte 2.1
Tofte 1 | Tofte 1.2
 | Tofte 1.1
Tilje 4 | 
Tilje 3 | 
Norne Structure and Zones
Horst structure (9x3 km) bounded faults
Laterally rather homogenous
Internal faults and carbonate cemented zones have a significant influence on the flow pattern
Barrier modelling is important
  Carbonate cemented layers
  Faults

## Slide 5: Norne Official Reserves & Production
STOIIP = 157 MSm3
Reserves = 95 MSm3
Ultimate RFo = 60.4%

## Slide 6: Subsea Development Solution - 1997
Norne FPSO
Subsea production/injection templates

## Slide 7: Subsea Development Solution - 2009
Norne FPSO

## Slide 8: Initial Development Strategy
Ca 200m
SW
NE
WI
GOC=2575m
WI/GI
Tilje Fm.
Tofte Fm.
Not Fm.
Not Sst.
Ile Fm.
OWC=2693m
GOC=2580m
OWC=2618m
Ca 7 km.
GI
Water
Gas
Oil

## Slide 9: Adjusted Development Strategy
Ca 200m
SW
NE
WI
GOC=2575m
WI/GI
Not Fm.
OWC=2693m
GOC=2580m
OWC=2618m
Ca 7 km.
WI/GI
Tilje Fm.
Tofte Fm.
Not Sst.
Ile Fm.
Water
Gas
Oil

## Slide 10
Adjustment of Strategy Over Time
water
1997 1998 2003 2006 2016-2021
Tofte Fm.
Not Fm.
L.Ile Fm.
U.Ile Fm.
oil
gas

## Slide 11: Integrated Use of 4D Seismic Data in Reservoir Management
Data acquisition strategy from the start
Seismic surveys: Base92 – 2001 – 2003 – 2004 – 2006 – 2008 – 2010 
Close cooperation with R&D and focus on competence development
Tight integration of 4D & Reservoir Engineering, for qualitative/quantitative
  History matching
  Mapping remaining oil

## Slide 12
Seismic modeling
Acoustic Impedance
Amplitude
Fluid Saturation
Acoustic Impedance
Amplitude
Fluid Saturation
4D Seismic
Simulation
Interpreted OWC
Extracted OWC
Rock model
Rock model
Inversion
4D Seismic Data & Flow Simulation Model
Notes: 12
Chance in any of these properties can be used to infer an oil-water contact
Currently, we often use difference in amplitude, AI and inferred oil-water contact to compare with those from the simulation model

## Slide 13: Qualitative use of 4D seismic in simulation model updating
old sim. model
4D data
Amplitude Diff (01-03)
AI Diff (01-03)
Sw Diff (Base-03)
Amplitude Diff (01-03)
Sw Diff (Base-03)
Amplitude Diff (01-03)
Notes: 13
Bottom-left: AI map; Red – increase in AI, increase in water saturation
OWC interpreted baesed on Amplitude difference event

## Slide 14
4D Diff (B-03)
Amplitude Diff (01-03)
updated sim. model
4D data
Sw Diff (Base-03)
Amplitude Diff (01-03)
AI Diff (01-03)
Pilot well
Pilot well
Qualitative use of 4D seismic in simulation model updating (cont’d)
Notes: 14
Magne: suggestion: copy slide 9 before this slide such that you can flip between the old and new model. Will highlight the changes.

## Slide 15
Quantitative Attempt of Using of 4D Seismic for Saturation Mapping
Sw
Change in AI
Sim Sw B-2006
4D Sw B-2006

## Slide 16: Summary
4D seismic data play an important role in calibrating Norne simulation models
4D data have been extensively used to identify remaining oil packets for infill drilling in Norne
Qualitative comparison of fluid fronts has been very useful & successful
Ongoing work toward quantitatively using 4D data
A large amount of data on Norne main field has been released to public research communities for research & innovations
Notes: 16
Magne: removed one point, added 2

## Slide 17: Thank you for your attention