## Slide 1: Rock Physics Analysis and Time-Lapse Imaging of the Induced Chemo-Mechanical Processes upon CO2 injection into Reservoir Rocks
Tiziana Vanorio
Stanford Rock Physics Laboratory
Notes: In this presentation I’ll give a snapshot of a very active part of our experimental program which aims at understanding the effect on seismic and transport properties of chemo-mechanical processes which occur in rocks when in presence of fluids that are non in equilibrium with the rock matrix.
The aim is quite broad as it spans from understanding how to enhance rock physics interpretation for 4D monitoring purposes to understanding the necessary building blocks to characterize the rock properties of carbonates and the evolution of their properties upon diagenesis.
In particular I’ll focus the presentation on the first aspect and on CO2 injection.

## Slide 2: 4D Seismic: Traditional Concept
time-lapse geophysical monitoring is based on the assumption that the time-variant changes in the images of seismic velocity depend on the variation of the properties of the rock frame and the fluid permeating it in response to changes in physical parameters such saturation, pore fluid pressure, temperature, and stress.
Notes: I mentioned 4D seismic: what’s the weakest link in our current workflow when interpreting time-lapse seismic data

## Slide 3: Fluid Substitution: Gassmann Model
saturation
free and dissolved gas
pore fluid pressure
temperature
Changes in rock seismic velocity and impedance are caused by a purely mechanical interaction between the fluid and the rock frame.
Water Saturated
Rock Seismic Velocity
Water Properties
Solid/Frame Properties
mineral composition
properties of the frame
F
porosity
ANY other fluid
Fluid Properties
r fl ; Kfl
r fl ; Kfl
r0
rdry
mdry
Kdry
Ko
Notes: This concept is more implicit when using Gassmann Model, the general tool of choice when interpreting the effect of a fluid on both log and seismic velocity data.

## Slide 4: CO2 Injection
Chemical Disequilibria: Fast and Time-dependent
Injection
Two days
After two days from the beginning of the injection an increased concentration of cations such as Calcium, Iron, and Manganese are measured at the observation well.
Notes: Time-lapse seismic monitoring is called upon to measure and quantify subsurface changes caused by geochemical processes due to the injection of fluids unlikely to be in chemical equilibrium with the host rocks.
The induced chemical disequilibria are fast, time dependent, and highly site-specific.
Problem: how to include these changes into seismic and rock physics data?

## Slide 5: Laboratory Program on CO2 Injection
Comprehensive Time-Lapse monitoring of:
changes in transport, elastic, and geochemical properties resulting from chemo-mechanical processes induced upon CO2 injection
    precipitation
    dissolution
changes in the rock microstructure: Time-Lapse high resolution imaging to quantify pore network modifications
    SEM images
    Ct-scan images

## Slide 6: Experimental Design
Injections are performed under reservoir pressure conditions : Pc up to 15-55 MPa and Pf up to 15-28MPa
  Magnitude and location of changes

## Slide 7: Rock Samples
Micritic Carbonates
Notes: micrite is characterized by large surface area; so it’s the most reactive phase in carbonate together with cement

## Slide 8: Pre-Injection Characterization
Mictrite Content
Notes: Similarly to clay in siliciclastics, the amount of micrite changes depending on depositional environment, it needs to be quantified

## Slide 9: Pre-Injection Characterization
Pore space in blue
Grayscale opacity
Reduced to show
Pore space
Pore Space and Its Connectivity

## Slide 10: Experimental Protocol
Ç√
Ç√
Pre-Injection
dry

## Slide 11: Monitored Properties
Chemical composition (pH, Cation Concentration) of the outlet brine (dissolution)
Porosity and permeability change upon injection (mechanical compaction)
P- and S- wave velocity upon injection and dry frame

## Slide 12: Velocity-Injected Pv-Pressure
Velocities of the dry rock frame after injection
DV
DP
DV
DP
Pre-injection
Pre-injection

## Slide 13: Porosity-Injected Pv-Pressure

## Slide 14: Time-Lapse SEM

## Slide 15: Time-Lapse SEM

## Slide 16: Selective Dissolution
25 mm
Before CO2 injection
After CO2 injection
25 mm

## Slide 17: Post-Injection Characterization

## Slide 18: Conclusions
Experimental data and pore scale images show that the seismic response of CO2 injection in brine-rock systems is far from being a pure fluid-substitution problem.
Fluid - rock chemical interactions affect the acoustic and transport properties of rock frame. This interaction implies a time-dependence of the properties of the rock frame in addition to those of the fluid permeating the rock (saturation, pressure…).

## Slide 19: Conclusions
Experiments shows where changes are likely to occur:
  cement dissolution at the grain contact  elastic modui
  porosity/density  elastic moduli
  the fraction of complaint pores seems to increase with injection as carbonates become more sensitive to pressure upon injection

## Slide 20: Where Are We Going?
saturation
free and dissolved gas
pore fluid pressure
temperature
Water Saturated
Rock Seismic Velocity
Water Properties
Solid/Frame Properties
mineral composition
properties of the frame
F
porosity
ANY other fluid
Fluid Properties
r fl ; Kfl
r fl ; Kfl
r0
rdry
mdry
Kdry
Ko
Amount of Dissolved Minerals
Notes:   Over the years 4D seismic has experienced tremendous developments: better data quality and resolution by installing permanent recording systems
  These efforts will be vain if we do not enhance data interpretation. Neglecting the occurrence of chemo-mechanical processes, their interdependency, and coupling with the rock microstructure and reservoir conditions leads to poor interpretation.

## Slide 21: Where Are We Going?
Notes: How Pore Network evolves upon injection of reactive fluids– Porosity-Permeability-velocity Trends

## Slide 22: Carbonate Rock Physics
Heterogeneous Microstructure

## Slide 23: Synthetic Samples

## Slide 24: Acknowledgments
Stanford Global Climate and Energy Project Award 55
DOE –NETL Project Award DE-FE0001159
Ingrain Inc., Houston, TX
ExxonMobil Upstream Research Co, TX
Petrobras, Brasil
Stanford Rock Physics & Borehole Consortium

## Slide 25: Conclusions
In carbonate rocks, velocity decreases mainly because of the formation of new, more complaint pores. Carbonates become more sensitive to pressure upon injection; i.e., the fraction of complaint pores increases.
Sandstones experience larger decrease in velocity as well as larger compaction than carbonates; velocity decreases because of dissolution of cement at the grain contacts.

## Slide 26: CO2 Injection in Sandstones
Velocities of the dry rock frame after injection

## Slide 27: Time-Lapse SEM

## Slide 28: Post-Injection Characterization

## Slide 29: Time-Lapse NMR
Larger Pores
Smaller Pores
T2 is inversely proportional to Surface/Volume ratio of the pore space
Pore coupling
“New pore space”
Tight Limestone
Micritic Carbonate
Grombacher and Vanorio, 2011- Geophysics

## Slide 30: Time-Lapse SEM