## Slide 1: The impact of partial CO2 saturation on seismic velocities of sandstones
By
Nicolaine Agofack, Andreas Bauer, Serhii Lozovyi
ROSE Meeting 24th – 27th April 2017
Acknowledgments: Rune M. Holt, Dawid Szewczyk, Pierre Cerasi, Øyvind Haave

## Slide 2
1. Problem statement
2. Tested material and experimental setups
Outline
3. Results and discussion
4. Modelling
5. Some conclusions

## Slide 3
Global climate change
Context : CO2 storage and monitoring
CO2 remains the most important of these gases (IPCC, 2007)
CO2 Capture and Storage (CCS)
Capture
Transport
Reservoir
a well
One of the major challenges is monitoring of CO2:
Mapping its movement in the subsurface
Demonstrating that it is stored safely in the reservoir
(Xue & Ohsumi, 2004)

## Slide 4
Time-lapse (4D) seismic is one of the powerful tools for monitoring and detection of leakage.
Context : Field frequency versus Lab frequency
(Murphy III, 1982)
Velocities of partially saturated rocks exhibit dispersion (change with frequency)
Seismic wave velocity also depend on:
Pore fluid and pore pressure
Degree of saturation of pore fluid
Differential pressure
Porosity and permeability of the rock, …
It is possible to measure the dynamic stiffness of a rock at seismic frequencies (in the lab), and seismic velocities are calculated under the assumption of a homogeneous rock mass and the absence of macroscopic dispersion effects (Spencer, 1981)

## Slide 5
Mixing of CO2 and water under high pressure at room temperature  CO2 dissolved into water.
Saturation procedure
n
Flowing of water saturated with CO2 into a sample under pressure slightly ( ̴ 5%) higher than the mixed pressure  Prevent CO2 to come out of water during this process.
n
n
Decreasing of pore pressure at constant differential stress and temperature  decrease of CO2 solubility and some CO2, called «free CO2» come out of the solution and is distributed at different regions of the sample (assumed homogeneous at mesoscopic scale).
n
n
n
Estimation of the degree of saturation of free CO2 for different decrease of pore pressure, (based on thermodynamic properties of CO2 and water)

## Slide 6
Experimental setups
Pore fluid lines:
Water
Water + dissolved CO2
Confining fluid line
Sample
Piston
Confining chamber
Strain Gauge
LVDT
Piezoelectric force sensor
Aluminium with strain gauge
Vin
Vout
Temperature Controller
TC1
TC2
Accum Mixer and Bottom Pp
Vacuum pump
V1
V2
V3
Ve
V4
V5
V6
Vv1
Vv2
Pg1
CO2 bottle
Accumulator
Mixer
P1
Evacuation (out of the Lab)
TC3
Triaxial cell
Water + CO2 mixing setup
After mixing, V6 and Vin are opened and
water + dissolved CO2 is injected
(refer to D. Szewczyk’s presentation)

## Slide 7
Experimental procedure
Loading path and CO2 Saturation.
Water
Vin
Vout
Axial stress
Pressures and stress
Confining pressure
Pore pressure
Axial stress
Test
Water-sat
5 MPa
12 MPa
14 MPa
14.5
7.5
16.5
5.5
12.5
14.5
Time
Flowing Water-CO2
Seismic frequency measurement
Sinusoidal stress applied: sample & aluminium
Strains εalu and εsam are measured by strain gauges
Axial stress : is constant
sam
Alu
Young modulus
Poisson ratio
Test
Water-sat
Test
W+CO2-sat
Water + dissolved CO2
Test
Presence of free CO2 (gas)

## Slide 8
Tested material and experimental setups
Property | Value
Diameter (cm) | 2.512
Length (cm) | 5.116
Cross-section (cm2) | 4.958
Weight (g) | 46.34
Density (g/cm3) | 1.847
Castlegate Sandstone was used in this experiment.
It has about 29% of porosity, composed of 70% quartz and contain no clay. Its permeability is around ̴ 10-14 m2 (10 mD)
Properties of the sample
4 strain gauges used
Sample with strain gauges

## Slide 9
Results and interpretation
Young modulus and Poisson ratio
Young modulus
Poisson ratio
Liquid-saturated sample
Partially Gas-saturated sample
The presence of “free” gas CO2 drops significantly the Young modulus and the Poisson ratio

## Slide 10
Results and interpretation
At ultrasonic frequency, P-wave velocity was evaluated from the travel time.
Evaluation of P- and S-wave velocities
Assuming that the sample is isotropic, homogeneous and linear elastic, P-wave and S-wave velocities are calculated from Young modulus, Poisson ratio and rock’s density.
No data
P-wave velocity
S-wave velocity

## Slide 11
Modelling / Isothermal or adiabatic conditions ?
Kf of the pore fluid needs to be evaluated in Gassmann model, specially in a closed system composed of water with dissolved CO2 + free CO2
Water saturated with CO2
Free CO2
dm
- dm
p
free CO2
Water with dissolved CO2
Due to dissolution of free CO2
Isothermal (zero frequency) with dissolution of CO2
Adiabatic without dissolution of CO2
Water saturated with CO2
Free CO2
p
Reuss average

## Slide 12
Test | ρsaturated rock (g/cm3) | Kfisot (GPa) | Kfadia (GPa)
water at 5MPa | 2.137 | 2.2394 | 
water at 7.5MPa | 2.138 | 2.2544 | 
water+CO2 at 7.5MPa | 2.142 | 2.1992 | 
2% free CO2 | 2.137 | 0.0268 | 0.3091
4.5% free CO2 | 2.130 | 0.0175 | 0.1326
10% free CO2 | 2.115 | 0.0106 | 0.0540
Modelling / Isothermal or adiabatic conditions ?
Kf of the pore fluid needs to be evaluated in Gassmann model, specially in a closed system composed of water with dissolved CO2 + free CO2
Bulk modulus Kf of the pore fluid is significantly affected by the presence of free CO2
The adiabatic modulus is more than 5 times higher than the isothermal one

## Slide 13
Biot-Gassmann Modelling
P-wave velocity
Data consistent with B-G model at seismic frequency
Dispersion at ultrasonic frequency needs to be considered
adiabatic
isothermal

## Slide 14
Biot-Gassmann Modelling
S-wave velocity
As assumed by B-G model, S-wave velocity is hardly affected by pore fluid.

## Slide 15
Conclusions
The measurements presented in this investigation were done on Castlegate Sandstone with 29% of porosity.
A seismic frequency, the presence of free gas CO2 in the pore space affects significantly the P-wave velocity and attenuation,
The results were consistent with Biot-Gassmann model.
For the sample with free CO2, significant dispersion was observed.
Dispersion fit and attenuation of P-wave simulated by Cole–Cole model gave a transition frequency at around 200 kHz.
S-wave velocity was hardly affected by pore fluid.
A ultrasonic frequency (Lab freq), the presence of free gas CO2 in the pore space affects hardly P-wave velocity.