## Slide 1: Low Frequencies for Inversion of Reflections
Lasse Amundsen, Ørjan Pedersen and Rune Mittet

## Slide 2: Outline
Motivation for tau-p inversion
Indirect tau-p inversion: FWI with Gauss-Newton scheme
Direct tau-p inversion: Scaling («AVA») and stretching («residial migration») the gradient of constant velocity inversion («c-v migration»)
Discussion/Conclusion
Hyperbolic reflections transform into ellipses, straight events into points.
Phase velocity

## Slide 3: Motivation for tau-p reflection inversion
Fast, elastic Newton-type inversions for VP, VS, density, attenuation …
Used where geology is «flattish»
  Unconventionals: «sweet spot» mapping
  Gas hydrates
  Temperature changes of water column
  Starting model for general FWI
Understand the potential, pitfalls, and limitations of FWI
  What can the gradient (of the misfit function) offer you “today”?
  Effect of missing low frequencies
Assumtions in this presentation
  Acoustic wave equation; constant density
  Known wavelet
Amundsen and Ursin 1991 F-K inversion of acoustic data: Geophysics 56 1027-1039
Zhao, Ursin and Amundsen 1994 F-K elastic inversion: Geophysics 59 1868-1881
Amundsen, Reitan and Arntsen 2005 Geometric analysis of data-driven inversion/depth imaging: JSE 14 51-62
Amundsen, Reitan, Helgesen and Arntsen 2005 Data-driven inversion/depth imaging: Inverse Problems 21 1823-50
Amundsen, Reitan, Arntsen and Ursin 2006 Acoustic AVA inversion/depth imaging: Inverse Problems 22 1921-45
Amundsen, Reitan, Arntsen and Ursin 2008 Elastic AVA inversion/depth imaging: Inverse Problems 22 1921-45

## Slide 4: I. FWI with Gauss-Newton method
In tau-p, the gradient can be found analytically when - the sum over frequencies ranges from – to + infinity - the wavelet is unity
Essentially, the gradient becomes a sum of step functions – which is great since it contains information about the velocity profile.
The high frequencies are not important.
Take out low frequencies, and the gradient will change.
Misfit function is sum over frequencies
Gradient of misfit function
Hessian
Model update

## Slide 5: Slab velocity model and tau-data for p=0
Model parameters M=100
# frequencies N=120 (up to 30 Hz)

## Slide 6: Gradient and velocity updates (GN inversion)
Start model: Constant velocity
Iterations 1,2,3 and 10
1
2
3
1
2
3
The gradients have layer or box- structure.

## Slide 7: Hessian and its inverse (iteration 10)
Since the gradients have layer-structure, the inverse Hessians do not need to do a big job. No stabilization is needed.

## Slide 8: Gradients without and with low frequencies
1
2
3
1
2
3
fmin=1.25 Hz
fmin<1.25 Hz
  “What can the gradient (of the misfit function) offer you “today”?”

## Slide 9: Velocity inversion without and with low frequencies
Both models produce «exactly» the same data and reduce misfit by
fmin=1.25 Hz
fmin<1.25 Hz

## Slide 10: II. Scaling and streching the gradient from constant-velocity inversion
Scaling g to get phase velocity v but in “squeezed” geometry;
Scaling = AVA
Stretching v to phase velocity in «correct» geomery;
Stretching = Residual migration
c1, v1 is water-speed velocity … note that scale and stretch depend only on gradient’s amplitude!
1
2
;

## Slide 11: Velocity model and data (p=0 and p=0.75/c1)
p=0
p=0.75/c1

## Slide 12: «Constant-velocity» gradients in pseudo-depth
Apply AVA to gradient :

## Slide 13: Scale gradients to phase velocity
:

## Slide 14: Residual migration («stretching»)
p=0
p=0.75/c1
:

## Slide 15: Discussion/Conclusion
Need low frequencies to calculate a gradient that carries information of layer velocities
The Hessian can partly correct the gradient for missing low frequencies
Scaling and stretching the gradient shown for plane-layer tau-p inversion – need generalization to laterally varying medium … tougher problem to handle