## Slide 1: Ultrasonic properties of creepy shales –for increased recovery and well abandonment
Presented by Rune M Holt, NTNU
Contributions from Audun Bakk, Andreas Bauer, Erling Fjær, Idar Larsen & Dawid Szewczyk + a few more
ROSE Meeting 24-25 April 2017

## Slide 2: Petroleum related Shale acoustics
Seismic: 4D monitoring of depleting / inflating reservoirs through overburden stress changes and strains
Ultrasonic / Sonic: Qualification of natural barriers outside casings to ensure appropriate sealing
Plus:
  Identification of source rocks or unconventional shale reservoirs from seismic
  Pore pressure prediction
  Use of sonic logs / seismic to assess shale strength for borehole stability during drilling

## Slide 3: Shale barriers
Field experience from more than 100 wells offshore Norway confirm shale barriers formed outside the casing.
Small scale laboratory experiments confirm that such barriers can be formed by creep / plastic deformation of shale.
«15 rigs full time in 40 years» to plug & abandon on all wells on the Norwegian Continental Shelf with conventional technology – natural barriers may be a tremendeous cost saver.
Need to know:
  The physical mechanisms controlling barrier formation
  Where it can be expected, and how to stimulate unwilling shales
  Verification of barriers (e.g. sonic & ultrasonic logs)
From Williams et al. (2009)
From E Fjær, SINTEF Petroleum Conference 2016 & 2017

## Slide 4: mechanisms
Similar to borehole stability: Stress concentration around the borehole (here: the annulus outside the casing) may lead to plastification / failure of the shale.
Creep accelerates when a rock approaches its state of failure.
Very large strain required to form a barrier!
Shale has nanoDarcy permeability and is likely to be less permeable than any cement (µDarcy range) even after it has failed.
For logging of shale barriers: What are the acoustic properties?
From E Fjær, SINTEF Petroleum Conference 2016 & 2017

## Slide 5: Ultrasonic velocities of a creepy field shale
Shale from  2 km depth; 28 % porosity, 44 % clay, about half is smectite.
Consolidated undrained (CU) triaxial tests with 3 samples from a given depth interval at 3 different confining pressures.
After failure, velocities become almost the same in all three tests (at different levels of confinement).
Note that shear stresses at failure are the same (friction angle  0).
Apparent slight increase in horizontal velocity after failure – implying that initial texture is manifested.
Holt et al., ARMA 2017

## Slide 6: Ultrasonic velocities of failed shales
Data are taken from ancient (1990’ies) borehole stability studies.
Not too different from initial velocities – hints that shale barriers may have ultrasonic properties similar to those of the initial shales.
Sonic logs can be used to assess properties of shale barriers, provided small dispersion between kHz and MHz.
Note: Acoustic impedance  4 – 10 … not too different from oil well cements
Holt et al., ARMA 2017

## Slide 7: Shales & stress
The experiment above – and several others – showed small stress & strain sensitivities for creepy shales.
Compared to e.g. sandstone, the difference is huge!
Possible explanation: µcracks in sandstone correspond to nano-cracks in shale – these are filled with water affected by the vicinity to solid surfaces and acts like a solid / viscous substance («bound water»).
Triaxial test with water saturated field shale core
Triaxial test with water saturated Castlegate sst

## Slide 8: Shales & stress
At stresses resembling in situ conditions, typical laboratory measured stress sensitivities are  10-3 MPa-1.
Still, we can see slow-down of seismic waves and S-wave splitting above depleting reservoirs, and can utilize it as fingerprints of the production scenario!
Data from isotropic tests published in the literature. The line segments represent stress intervals where stress sensitivity was estimated, and where velocity changed linearly with stress.
Hatchell & Bourne, 2005
Barkved & Kristiansen, 2005

## Slide 9: Overburden Stress Path
Pore pressure changes in a reservoir (depletion / inflation) cause stress (and pore pressure) changes in overburden and surrounding rock.
The zone of influenced overburden is large – so even small velocity changes add up to measurable 2-way travel time changes.
Oil / Gas
Depletion

## Slide 10: Overburden stress path
Geertsma (1973) (based on linear elasticity and no contrast between reservoir and surroundings) predicted constant mean stress path. Stress arching (gv > 0) above the reservoir increases with decreasing aspect ratio of the depleting zone.
Stress arching increases if overburden is stiffer than the reservoir. Notice that both vertical and horizontal stress may decrease (gh > 0) if overburden is more than twice as stiff than the reservoir.
Reservoir tilt promotes arching.
Non-elasticity (plasticity, faulting) will affect the stress path further.

## Slide 11: Laboratory experiments with shale cores
Normally laboratory experiments are performed along one stress path only (usually hydrostatic).
Here: 4 different undrained stress paths are applied near the in situ stress state of field shale cores.
CMS (k=-½): Constant Mean Stress
3AX (k=0): Uniaxial stress
K0 (k=K0) : Uniaxial strain
ISO (k=1): Incremental isostatic
ISO
3AX
K0
CMS
We denote laboratory stress path:

## Slide 12: The impact of stress path
Fully saturated field shale (24 % porosity, 76 % clay).
Linearity of stress sensitivity with stress path – a direct consequence of linearity in velocity change with stress.
The influence of stress path is significant!
Only axial P-wave shown – but also other modes show linear trends.
Chart: Stress Path Dsr/Dsz [-]
| 1.0004167952266929 | 8.7112626591082922E-5 | 0.65588412132434437 | -0.49925361519813205
B Shale | 0.0010613 | 0.00051225 | 0.00079488 | 0.00039108

## Slide 13: The impact of stress path
The dilation factor or R-parameter is a measure of strain sensitivity:
Strain depends on stress path (by Hooke's law in linear & isotropic elasticity)=>
High stress path  small axial strain => High R value
Chart: Stress Path Dsr/Dsz [-]
| -0.5 | 0 | 0.65724891266085073 | 1
 | 2.0855 | 3.1965 | 8.6022 | 18.1629

## Slide 14: the Role of pore pressure
Pore pressure change during undrained loading / unloading also follows a linear relationship with the stress path.
This is in accord with the behavior suggested by Skempton (1954), and permits determination of 2 parameters (Skempton’s A & B).
The overburden response to reservoir pore pressure change is undrained, i.e. it can be estimated from the in situ stress path + Skempton’s A & B.

## Slide 15: Linking to 4D response
Combining:
  Laboratory measured stress path sensitivity of velocities
  Skempton’s pore pressure parameters
  In situ stress path from geomechanical modelling
  => In situ velocity change & R-factor vs reservoir pore pressure change
Note: Stress sensitivity at seismic frequencies may be different from ultrasonic, as seen in low frequency experiments with shale during PhD work by Dawid Szewczyk and Serhii Lozovy.

## Slide 16: Linking to 4D response
We relate the velocity change to the change in reservoir pore pressure, accounting for pore pressure change in the overburden:
Skemtpon’s Bs=1 for soft & fully saturated shale
Bs=0 corresponds to a «dry» (or drained case)
In the drained case, stress sensitivity from porosity change has to be added

## Slide 17: conclusions
Stress path dependent stress sensitivity of velocities and pore pressure response in shale combined with geomechanical modelling enables prediction of in situ 4D response.
  The R-factor in a given geological formation is largely controlled by the vertical strain trhough the stress path.
The low stress sensitivity of velocities in soft shales makes it possible to predict sonic / ultrasonic properties from logs.
  This may facilitate the detection of shale barriers around cased boreholes for P&A.
The fundamentals of stress sensitivity in shale is not fully understood - nano-scale influence appears to play a role.

## Slide 18: acknowledgements
The authors would like to acknowledge financial support from The Research Council of Norway and a number of industry partners for:
The KPN-projects “Shale Rock Physics: Improved seismic monitoring for increased recovery” and “Logging of Shale Barriers” at SINTEF Petroleum Research.
The ROSE program at NTNU

## Slide 19
4th International Workshop on Rock Physics; Trondheim, Norway 29 May – 2 June 2017
More than 70 papers by researchers from almost all continents
20 hours of daylight…
https://www.ntnu.edu/4iwrp