## Slide 1: 4D prestack time shifts
Thomas Røste (Statoil) and Martin Landrø (NTNU)
ROSE-meeting
April 2017

## Slide 2: Outline
Introduction: Time shifts vs offset
Field examples with time shifts varying with offset:
  Valhall; Reactivated fault
  Block 2/4; Gas-effect
  Snorre; Geomechanical changes
Discussion / Conclusions

## Slide 3: Outline
Introduction: Time shifts vs offset
Field examples with time shifts varying with offset:
  Valhall; Reactivated fault
  Block 2/4; Gas-effect
  Snorre; Geomechanical changes
Discussion / Conclusions

## Slide 4: Scenarios for seismic ray paths
Sea Surface
Seabed
Top Reservoir
Base Reservoir
Velocity change
Depth
*
*
Time shifts appear on near offsets, but not for far offsets.
Might vanish on full stack
Reservoir changes
Notes: Time shifts typically accumulate with depth

## Slide 5: Scenarios for seismic ray paths
Sea Surface
Seabed
Top Reservoir
Base Reservoir
Depth
Time shifts appear on far offsets,
and might appear on full stack
*
*
Velocity change
Reservoir changes

## Slide 6: Scenarios for seismic ray paths
Sea Surface
Seabed
Top Reservoir
Base Reservoir
Velocity change (reactivated fault)
Velocity change (production-induced stress changes)
(reflector)
Depth
Time shifts appear on far offsets,
and might appear on full stack
*
*
Overburden changes

## Slide 7: Scenarios for seismic ray paths
Sea Surface
Seabed
Top Reservoir
Base Reservoir
Velocity change (reactivated fault)
Depth
Velocity change (production-induced stress changes)
Time shifts not present on far offsets,
and might vanish on full stack
*
*
(reflector)
Overburden changes

## Slide 8: Synthetic 2D example (reservoir changes)

## Slide 9: 2D synthetic model (Snorre)
Vp, Base model
Notes: Fig from Marianne Houbiers

## Slide 10: FD-modelling
Reservoir changes: Water replacing oil
Notes: Finite difference modelling:
Time-lapse reservoir changes: Rise in OWC

## Slide 11: Time shifts; near offsets
Reservoir changes: Water replacing oil
10-17 degs

## Slide 12: Time shifts; near-mid offsets
Reservoir changes: Water replacing oil
17-22 degs

## Slide 13: Time shifts; mid offsets
Reservoir changes: Water replacing oil
22-27 degs

## Slide 14: Time shifts; far offsets (27-32 degs)
Reservoir changes: Water replacing oil
27-32 degs

## Slide 15: Time shifts; ultrafar offsets
Reservoir changes: Water replacing oil
32-40 degs

## Slide 16: Time shifts; full offset stack
Reservoir changes: Water replacing oil
10-40 degs
Notes: Full stack time shifts influenced by all offset stacks.
Will again influence time strains and estimates of velocity changes.
For full-stacked time shifts, the offset-variation is lost and, in addition, far-offsets might induce artefacts and influence the interpretation of full-stacked time shifts.

## Slide 17: Outline
Introduction: Time shifts vs offset
Field examples with time shifts varying with offset:
  Valhall; Reactivated fault
  Block 2/4; Gas-effect
  Snorre; Geomechanical changes
Discussion / Conclusions

## Slide 18
Gas Cloud
N
Investigated line,
LoFS 1-3
Røste et al., 2007
NORWAY
North
Sea
Valhall
DENMARK
Valhall Field
Map of top reservoir
Notes: Placement of investigated line is highly inaccurate here.

## Slide 19: Time shifts @ top reservoir (position vs offset)
Buried anomaly
Investigated in detail
Gas cloud
Gas cloud
Røste et al., 2007
Valhall

## Slide 20
Time shifts vs offset @ top res. for 6 positions
Røste et al., 2007
position 1.55 km
position 1.60 km
position 1.65 km
position 1.80 km
position 1.75 km
position 1.70 km
The time shift “distortions” move with offset as position increases
Valhall
Notes: Picked time-shifts (versus offset) between survey 1 & 3 for 6 positions.

## Slide 21
SE
NW
Top
Reservoir
Max velocity
decrease (25 m/s) at depth 1.9 km
Synthetic model: Velocity change
Position (km)
∆Vp (m/s)
0
-5
-10
-15
-20
-25
Initial velocity-model:
Constant = 1950 m/s
Sea Surface
Valhall
Røste et al., 2007
Notes: The simulted growing fault has longer extent in the vertical than the lateral direction, and is also tilted,
which is necessary to capture the picked (relative) time shifts.

## Slide 22
Blue solid line: Time shifts from synthetic model
Røste et al., 2007
position 1.55 km
position 1.60 km
position 1.65 km
position 1.80 km
position 1.75 km
position 1.70 km
Synthetic model induces time shifts (blue line) matching the observations (red crosses)
Valhall

## Slide 23
Coherency time-slice at 1960 ms
m
N
1.0 km
Receiver line used
in this study
Younger red fault (strike slip) cuts the older yellow fault
Location of shallow 4D distortion zone
Valhall
Røste et al., 2007
Notes: Coherency map created from Valhall streamer data (2002)

## Slide 24
RMS amplitude changes at top res.
m
N
1.0 km
Reasonable that red fault grow at the SW tip
Large amplitude changes
indicate compacting zones
Receiver line used
in this study
Younger red fault (strike slip) cuts the older yellow fault
Location of shallow 4D distortion zone
Valhall
Røste et al., 2007

## Slide 25: Outline
Introduction: Time shifts vs offset
Field examples with time shifts varying with offset:
  Valhall; Reactivated fault
  Block 2/4; Gas-effect
  Snorre; Geomechanical changes
Discussion / Conclusions

## Slide 26: SAGA-wells 2/4-14 and 2/4-15
NORWAY
North
Sea
Valhall
DENMARK
TOR
EKOFISK
ALBUSKJELL
2/4-14
2/4-15
Ekofisk
Investigated line

## Slide 27: SAGA-wells 2/4-14 and 2/4-15
2/4-14
2/4-15
7 km
Time (s)
PhD work of Andreas Evensen, NTNU, 2012
3D (1991) seismic section
0.2
0.4
0.6
0.8
Investigated reflection
Notes: Prospect. Production never started.
3D seismic from 1991. Reservoir depth around 4.7 km.

## Slide 28
Time shifts (1988-1990) near well 2/4-15 – using 4D tomography
PhD work of Andreas Evensen, NTNU, 2012
Modelled time shifts vs offset
Offset (km)
0.2
0.4
0.6
0.8
1.0
5
4
3
2
1
0
Real time shifts vs offset
Offset (km)
0.2
0.4
0.6
0.8
1.0
2/4-15
5
4
3
2
1
0
Initial model
0.0
-0.1
-0.2
-0.3
Depth (km)
0
0.1
0.2
0.3
0.4
0.5
2/4-15
Final model
Depth (km)
0
0.1
0.2
0.3
0.4
0.5
0.0
-0.1
-0.2
-0.3
2/4-15
Misfit versus # iterations
Notes: Here are the prestack time shifts for the reflector shown at last slide.
Andreas modelled time shifts from an initial model, and by obtaining the misfit between modelled and real prestack time shifts, he updated the initial velocity change model.
After several iterations, he obtained a final velocity model. The final model shows a chimney-like (“pipe”) velocity change.
(Modelled time shifts of the final velocity model are given bottom left.)
Final figure shows the misfit between modelled and real time shifts versus the nr of iterations.

## Slide 29: Outline
Introduction: Time shifts vs offset
Field examples with time shifts varying with offset:
  Valhall; Reactivated fault
  Block 2/4; Gas-effect
  Snorre; Geomechanical changes
Discussion / Conclusions

## Slide 30: Time shifts (97-09) @ top reservoir; Snorre Field
slow-down
speed-up
Investigated inline
NORWAY
Bergen
Stavanger
North
Sea
Snorre
Time shifts caused by overburden velocity changes due to pressure depletion
Notes: Stacked time shifts map

## Slide 31: Poststack time shifts, IL 4800
5500 5400 5300 5200 5100 5000 4900
XL
Hordaland
Balder
Top reservoir
SN6.4
SN9.3
SN3.4
Well P-45
Well A-6H
Gas-injection
Overburden stretch
Influence from far offset time shifts?
Offset 3 km
?
slow-down
speed-up
Investigate @ TWT 2.9 s
TWT (s)
1.0
2.0
3.0
Snorre
Notes: P-45: WAG-injector (01-)
Exact TWT: 2.923 s
Note! TS (96-06)
IL 4800

## Slide 32: Prestack time shifts, IL 4800 @ TWT 2.9 s (XL vs Offset)
Snorre
Figure cut out
Notes: Note! TS (96-06)
IL 4800

## Slide 33: Outline
Introduction: Time shifts vs offset
Field examples with time shifts varying with offset:
  Valhall; Reactivated fault
  Block 2/4; Gas-effect
  Snorre; Geomechanical changes
Discussion / Conclusions

## Slide 34: Discussion / Conclusions
Time shifts varying with offset
  Induced by velocity changes with small lateral extent
    Reactivated faults
    Leakage or out-of-zone injection
    Overburden stress changes
    Reservoir changes
Poststack time shifts
  Offset-variation is lost
  Small velocity changes might not be detected
  Far offset time shifts might appear as artefacts
Valhall
2/4-14
Snorre

## Slide 35: Acknowledgments
Andreas Evensen and Marianne Houbiers for input figures

## Slide 36
Prestack time shifts
Thomas Røste
Geophysicist
E-mail: thros@statoil.com
Tel: +47 90260006
www.statoil.com