## Slide 1
Accelerating 3D Elastic Wave Equations on Knights Landing based Intel Xeon Phi systems
[nvidia.com]
Mohammed Sourouri1
Espen Birger Raknes2,3
Norwegian University of
Science and Technology (NTNU)
April 25, 2017
1 Department of Electronic Systems
2 AkerBP 3 Work conducted when part of Department of Geoscience and Petroleum
Notes: What you see on the picture is NVIDIAs latest GPU offering, the P100.
For the last decade or so, GPUs have been adopted by the scientific community at a steady rate.
Owning to their parallel architecture,
GPUs have thus been adopted by both the scientific community and the industry to accelerate different types of computations.

## Slide 2
Accelerating 3D Elastic Wave Equations on Knights Landing based Intel Xeon Phi systems
[nvidia.com]
[openacc.org]
[opencl.org]
Mohammed Sourouri1
Espen Birger Raknes2,3
Norwegian University of
Science and Technology (NTNU)
April 25, 2017
1 Department of Electronic Systems
2 AkerBP 3 Work conducted when part of Department of Geoscience and Petroleum
Notes: Although GPUs can indeed accelerate many types of applications.
Programming them appears to be a very challenging task, which unfortunately excludes many domain scientists.
The three most common way of programming Nvidia GPUs is to either use
a programming extension to C/C++ and Fortran called CUDA or a directive based model called OpenACC.
OpenACC is simpler than CUDA but getting really good performance using OpenACC is difficult.
The third and probably the most complicated way of programming GPU is to use the OpenCL programming extension.
OpenCL is in many ways similar to CUDA but involves many more low-level details.
In short, we have a device that delivers tremendous amount of performance, but that can only be unlocked by experts.

## Slide 3
Accelerating 3D Elastic Wave Equations on Knights Landing based Intel Xeon Phi systems
[newsroom.intel.com]
Mohammed Sourouri1
Espen Birger Raknes2,3
Norwegian University of
Science and Technology (NTNU)
April 25, 2017
1 Department of Electronic Systems
2 AkerBP 3 Work conducted when part of Department of Geoscience and Petroleum
Notes: The machine you see on this picture is Intel’s alternative to GPUs.
It is called Xeon Phi and shares certain similarities with GPUs.
While GPUs are accelerators, which means it cannot operate with a general-purpose CPU,
the latest generation of Xeon Phi are self-hosted systems.
This means that one no longer needs to take care of intricate details w.r.t. moving data between the CPU and the GPU.
Moreover, conventional and much-used programming language such as C/C++/FORTRAN or models such MPI and OpenMP can be used.
The focus of this talk is on parallel computing on the Xeon Phi using OpenMP.

## Slide 4
Accelerating 3D Elastic Wave Equations on Knights Landing based Intel Xeon Phi systems
 | Tesla P100 | Xeon Phi
FP32 SP | 9.3 TFLOP/s | 6 TFLOP/s
FP64 DP | 4.7 TFLOP/s | 3 TFLOP/s
Memory bandwidth | 549 GB/s | 475 GB/s 90 GB/s (DDR4)
Memory capacity | 16 GB | 16 GB 384 GB (DDR4)
Mohammed Sourouri1
Espen Birger Raknes2,3
Norwegian University of
Science and Technology (NTNU)
April 25, 2017
1 Department of Electronic Systems
2 AkerBP 3 Work conducted when part of Department of Geoscience and Petroleum
Notes: So far we have talked about the architecture of the Xeon Phi, but not about its theoretical peak performance.
Let us see how it compares to the latest and the greatest generation of GPUs from Nvidia.
In terms of raw performance, there is no doubt that the P100 is faster than the Xeon Phi.
Xeon Phi’s main advantage is that it can store more data thanks to the addition of DDR4 data.
Having said that, things are a bit more complicated than that.
First of all, as already mentioned, harnessing performance out of the P100 can be quite challenging.
On the other hand, Intel promises that using a programming model such as OpenMP, is sufficient to achieve good performance.
Secondly, writing GPU applications requires a significant software engineering effort.
Xeon Phi on the other hand is binary compatible with x86 code, which means that you can run your existing applications on Xeon Phi without changing as much as a single line of code.
Machine balance

## Slide 5
This presentation focuses on exploring the use of KNL based Xeon Phis for accelerating 3D Seismic Wave Simulations
3D Seismic Wave Simulator
Results
Xeon Phi Architecture

## Slide 6
This presentation focuses on exploring the use of KNL based Xeon Phis for accelerating 3D Seismic Wave Simulations
3D Seismic Wave Simulator
Results
Xeon Phi Architecture
Notes: In this presentation, I will talk briefly about our target application.

## Slide 7
This presentation focuses on exploring the use of KNL based Xeon Phis for accelerating 3D Seismic Wave Simulations
3D Seismic Wave Simulator
Results
Xeon Phi Architecture
Notes: Then, I will provide a high-level overview of the KNL based Xeon Phi architecture.

## Slide 8
This presentation focuses on exploring the use of KNL based Xeon Phis for accelerating 3D Seismic Wave Simulations
3D Seismic Wave Simulator
Results
Xeon Phi Architecture
Notes: Finally, I will present some early results, in which we compare our Xeon Phi results with multi-core CPU results.

## Slide 9
Target application: A 3D Seismic Wave Simulator developed from ground-up at NTNU
Numerical framework1
Staggered-grid explicit FD
8th order in space
2nd order in time
3D elastodynamic wave equation
Memory-bound stencil application
parallelized using OpenMP
1 Espen Birger Raknes, Børge Arntsen, and Wiktor Weibull. 2015. Three- dimensional elastic full waveform inversion using seismic data
from the Sleipner area. Geophysical Journal International 202, 3 (2015), 1877–1894. DOI: https://doi.org/10.1093/gji/ggv258
Notes: The application is written in C++14 and parallelized using OpenMP.

## Slide 10
Vx
Vy
Vz
SxxSyySzz
dxf
dzb
dyb
dyf
dzb2
dxb
dzf
dxb2
dyb2
Sxy
dyf2
dxf2
Sxz
dxf3
dzf3
dxb3
dyb3
dzb3
There are in total 25 kernels that needs to be computed for each loop iteration.
Syz
dzf2
dyf3
Target application: A 3D Seismic Wave Simulator developed from ground-up at NTNU

## Slide 11
KNL based Xeon Phi: A cluster on chip
2D mesh interconnect
Tile
Each tile consists of two x86 cores
Communication via a 2D mesh interconnect
Core
Each core has two 512 bit vector processing units (VPUs)
Private 32KB L1 cache
1MB shared L2 cache
Memory
8x2GB MCDRAM
Up to 384 GB DDR4 memory (three channels)

## Slide 12
The memory architecture of KNL based Xeon Phis is user-configurable.
MCDRAM
(CACHE)
DDR4
Cache mode
MCDRAM
(CACHE)
DDR4
Flat mode
KNL
KNL
Notes: The memory architecture of KNL is user-configurable and can be set in three modes: cache, flat and hybrid.
The two most important are cache and flat mode.
I will not cover hybrid in my talk today.
Also, I will not mentioned the various cluster modes.
Changing the memory architecture requires that the system has to be rebooted.
Cache mode requires the least work, as the MCDRAM acts as cache for read/writes between the cores and the DDR4 memory.
If you want to just run your code on the KNL, this is the most interesting mode.
If you have a memory-bound application, then the highest memory bandwidth can be achieved using flat mode.
One downside of this mode is that you need to either use a tool such as the memkind library to mange memory allocations or use a tools such as numactl to take care of non-uniform memory access.
If your application workload does not fit into the MCDRAM, then the application will seg fault.

## Slide 13
[olcf.ornl.gov]
1.8x
1.6x
1.3x
Baseline Xeon Phi results compared to a highly-tuned multi-core implementation.
Notes: For our first experiment, we are interested in establishing a baseline for future reference.
Here, we have taken a highly-tuned multi-core CPU code and compiled it for KNL.
Our metric of choice is Mega Lattice Update per Second, which describes how many grid point is updated per second.
The formula for computing the MLUPS is, number of iterations x Nx x Ny x Nz * 1e-6 / elapsed_seconds
The memory model is cache.
In other words, the MCDRAM is used for caching transactions to the DDR4 memory.
Unsurprisingly, the smaller the workload size, the better performance.
The reason for this is because more data fits in the MCDRAM.

## Slide 14
[olcf.ornl.gov]
By tuning the thread affinity, we can can further increase the performance.
1.99x
1.7x
1.3x
Notes: The default thread affinity policy on the KNL is to scatter the threads.
Although this works very well for many memory-bound applications, this is not the best affinity policy for our application.
Hence, it is worth exploring other affinity policies.
By using the compact affinity policy, we are able to improve the performance further.
Again, we see that the smallest workload size enjoy the most of such a change.
When using the compact thread affinity, neighboring thread can share data, leading to a more efficient data sharing via local caches.

## Slide 15
[olcf.ornl.gov]
Changing the memory policy (cache->flat) can have a dramatic impact on the performance.
2.33x
1.8x
1.4x
Notes: The reason why the smallest problem size enjoys the best performance is because the entire problem size fits in the MCDRAM.
For the larger problem size, we have only placed the most important arrays in the MCDRAM, while we have let other less important arrays spill into DDR4.

## Slide 16
In summary, we have shown that KNL can increase performance compared to multi-core x86 CPUs significantly
KNL provides a good blend of ease-of-use and performance
If the entire workload fits into MCDRAM, use flat mode, else cache mode is always a safe choice.
We have demonstrated that high performance can be achieved with only few steps.