## Slide 1: On some unsolved issues in shale rock physics How do we model compaction, cementation and uplift of shales?
Per Avseth, NTNU/G&G Resources
ROSE Meeting April 23rd 2018

## Slide 2: Motivation: Why are shales important in QI?
Shales comprise most of the overburden rocks.
Normal compaction trends of shales can be used to estimate uplift.
Shales define the background trend in AVO data
Shales, as cap-rocks, impacts the AVO reflectivities of top and base of reservoirs.
Organic-rich shales are the most common source rocks.
Intra-reservoir shales contribute to reservoir heterogeneity, baffles and barriers for fluid flow.
Terracotta Army, Xian, China (200 bC).

## Slide 3: Key issue: How to extrapolate shale properties away from wells?
How do we extrapolate elastic properties of shales away from wells?
How do we best model rock physics properties of shales during burial and uplift? (Porosity and velocity versus depth).
How do we take into account stress sensitivity in shales?
How do we best model chemical compaction and cementation in shales?
How do we discriminate depositional trends and diagenetic trends in shales?

## Slide 4: Sand and shale compaction trends in the North Sea
Quartz cementation starts at around 70 degrees C. Hence, North Sea Paleocene sands can both be unconsolidated and cemented. Shales transform from smectite-rich to illite-rich at around the same temperature.

## Slide 5: Mechanical versus chemical compaction of shales. Experimental observations (Mondol et al. 2008) and rock-physics modeling (Dræge et al., 2006).

## Slide 6: Documentation of chemical compaction and quartz cementation in shales.
Storvoll and Brevik, 2008
Thyberg et al., 2009

## Slide 7: Depth trend modeling of shales (Avseth et al., 2008)

## Slide 8: Rock physics and AVO modeling constrained by burial history
Vp/Vs
Acoustic Imp.
Porosity
Cement volume
1. Burial history
Burial depth (m)
Temperature (degrees C)
Geologic Age (M.Yr)
0
250
Stø Fm
Deposition
Max. burial
(Present day burial)
2. Diagenetic modeling (Walderhaug)
Depth/Temperature
Onset cement
3. Rock physics modeling (Dvorkin-Nur)
Depth/Temperature
Oil
Brine
Oil
Brine
4. AVO modeling (Zoeppritz)
+ shale
compaction
and RP
Intercept
+
-
+
-
Gradient
Deposition
Brine
Oil
Shale (Background)
Max. burial

## Slide 9: A «typical» present day geo-section offshore Norway
Quarternary sediments
Sea water
Miocene sediments
Oligocene-Eocene
Paleocene
Cretaceous
Syn-rift
Jurassic/Triassic
Prospect A
Prospect B
Prospect C
Discovery
70 C
Cenozoic uplift
Increasing landward

## Slide 10: «Restoring» geo-section to maximum burial. Have prospects been into the frying pan?
The “Frying Pan”
(T>70 C required for Qz-cem. )

## Slide 11: Burial constrained AVO modeling at “Discovery” well. (Campanian sands w/oil give AVO class III)
“Frying pan” (chemical compaction/Qz cementation)
Brine sst
Oil
Oil
Brine
Shale
Shale
Brine
sand
Burial
curve
70 C
Fluid trend
Compaction trend
Brine
Oil

## Slide 12: Burial constrained AVO modeling at prospect C (Aptian sst) Oil-filled sst = AVO class IIp
“Frying pan”
Brine sst
Oil
Brine sst
Oil
Fluid trend
Compaction trend
Oil
Brine
Shale
Shale
Brine
sand
Burial
curve
70 C

## Slide 13: Barents Sea Example: Acoustic impedance (water-saturated) vs. porosity along south-north well log profile
Uplift map
(Johansen, 2017)
Uplift=ca.1400
Uplift=ca1800
Contact cement
Increasing cement
Illitization
+ micro-xst qz
Sandstones of Stø Fm are getting increasingly stiffer northwards, likely related to increasing maximum burial. Fuglen shales show a significant trend change in northern wells (Atlantis and Apollo), likely related to illitization and micro-crystalline cementation of shales (see Thyberg et al., 2009; Storvoll and Brevik, 2008).
5% cement
2% cement
0.5% cement

## Slide 14: Expected AVO signatures at Top Stø: Class III AVO for both oil and gas.
Gas
Oil
Brine

## Slide 15: Zoomed in further: Expected AVO class IIp-II for oil and gas.
Gas
Oil
Brine

## Slide 16: Hoop Area – Burial history affect seismic signatures (due to changes in both shales and sst)
NW
SE
Hanssen
AVO class III
AVO class I
AVO class IIp
Data courtesy of TGS

## Slide 17: Schematic illustration of burial history, rock consolidation and AVO signatures
Chemical compaction
Mechanical
compaction
1000m
2000m
3000m
600m
1600m
2600m
Total depth
Burial
depth
Sea water (ca. 400m)
T= ca. 70C
(= ca. 2000m)
Ca. 1800m
uplift
Ca. 1500m
uplift
Top Stø today
Top Stø (max burial)
Cemented Sst (hard seismic response)
Loose sand (soft seismic response)
Transition zone

## Slide 18: Shale depth trends (w/uplift) in Hoop area Fuglen Fm (cap-rock of Stø Fm)
Wisting Central
Atlantis
Smectite  Illite
Clay  Qz

## Slide 19: Rock physics modeling of Wisting and Atlantis caprock shale (Fuglen Fm)
Chemical compaction
and/or Qz increase
Qz
Mechanical compaction

## Slide 20: The road ahead – Improved understanding of shale RP properties during burial and uplift
dVp/dP
Depth
Mechanical compaction
Chemical compaction
Tectonic uplift
and brittle failure (cracks)
?
Interesting issues to consider:
Can we apply a Walderhaug-type cement model for shales? (Cementation both during subsidence and uplift if T>Tc)
Can more realistic shale trends give better velocity and anisotropy predictions?
Do we need to honour stress anisotropy during uplift?
Implications for seal integrity?