## Slide 1: Cavity cloud generated by seismic air-gun arrays ̶ comparing video recordings to modeling
Babak Khodabandeloo PhD Candidate (NTNU)
babak.khodabandeloo@ntnu.no
Supervisor: Prof. Martin Landrø
Rose Meeting
23 April 2018

## Slide 2
Field Measurement with a Broad-band Hydrophone (125 kHz):
Background Noise
Single Air-gun 300 in3
Single Array 1500 in3
Full Array 2730 in3 (with three sub-arrays)
Why only the Full array has a high-frequency content?
Notes: Lets look at the energy spectrum of recorded signals by the broad-band Hydrophone.
How can we explain the high-frequency content of full array?

## Slide 3
Source is a full air-gun array.
Notes: It is by a vessel along a straight line above the hydrophone

## Slide 4
Underlying mechanism for high-frequencies (>10 kHz) in seismic air-gun arrays?

## Slide 5
Ghost cavitation hypothesis by Martin Landrø et al. (2011)
3m
6m
4 bar
@ 1m
4 bar
@ 1m
+
+
̶
̶
3m
3m
2m
O
(-0.65) + (-0.65) + 1.2 = -0.1 bar!
Pressure at point O:
Notes: Assuming each Air-gun generates a peak pressure of 4 bar at 1m, the pressure at point A due to the reflection from sea surface will be -1.3 bar.
At that point the hydrostatic pressure is around 1.2 bar. Using linear theory the mean pressure is negative!! and consequently cavitation will occur at point A.

## Slide 6
Where and When?
Individual Cavity Signatures
Propagation of Cavities
Superposition of Cavities
Khodabandeloo, B., Landrø, M. and Hanssen, A., 2017. Acoustic generation of underwater cavities—Comparing modeled and measured acoustic signals generated by seismic air gun arrays. The Journal of the Acoustical Society of America, 141(4), pp.2661-2672.
Ghost Cavitation Cloud Modeling Technique:

## Slide 7
Total Pressure
Estimating pressure around a seismic air-gun array:

## Slide 8
Response of a microbubble to the pressure variations at points A and B:
Point B
Point A
: the time dependent radius of the cavity,
: density and sound speed of undisturbed water,
is the dynamic viscosity of water.
: water surface tension
: The pressure inside the cavity,
: external pressure
Bubble dynamics equation (Prosperetti and Lezzi, 1986):

## Slide 9
Field measurement
Simulation results
Khodabandeloo, B., Landrø, M. and Hanssen, A., 2017. Acoustic generation of underwater cavities—Comparing modeled and measured acoustic signals generated by seismic air gun arrays. The Journal of the Acoustical Society of America, 141(4), pp.2661-2672.
Notes: When Cavity appears & its lifespan

## Slide 10
10
Gun
13 & 14
Gun
11 & 12
Gun
15 & 16

## Slide 11
11
Notes: Four Successive images extracted from video recording:

## Slide 12
Modeled Cavity cloud:
12

## Slide 13
13

## Slide 14
14
Khodabandeloo, B., and Landrø, M., Acoustically induced cavity cloud generated by air-gun arrays ̶ comparing video recordings and acoustic data to modeling. Submitted to The Journal of the Acoustical Society of America.

## Slide 15
Conclusions
Thanks Statoil and CGG for funding the experiments presented here. This research is funded by ARCEx partners and the Research Council of Norway (grant number 228107).
Acknowledgment
The first convincing photographic evidence of ghost-induced cavitation
Reliable modeling technique for ghost cavitation phenomenon.
Ongoing research
Acoustic properties within the cavity cloud
Calibrating the numerical model
Future work:
Notes: To the best of our knowledge,

## Slide 17
17
Notes: Four Successive images extracted from video recording:

## Slide 18
Modeled Cavity cloud (all air-gun activated simultaneously) :
18

## Slide 19
19
Gun
13 & 14
Gun
11 & 12
Gun
15 & 16

## Slide 20
Air-gun:
High Pressure Air (~137 bar)
Air-gun Ports
Shuttle
20
Notes: Seismic air guns were developed in the 1960s to replace
dynamite as a sound source for geophysical exploration
Airgun: The most common (>95%) and efficient marine seismic source.
>> An air-gun generates acoustic pressure waves from expansion and contraction of an air bubble which is formed by releasing high-pressure air (typically 2000 psi) into the surrounding water within a short time