## Slide 1: ROSE meeting April 23rd, 2018
PhD candidate: Serhii Lozovyi
Supervisor: Prof. Andreas Bauer
Relating static and dynamic stiffness of shales: effects of frequency and stress
Notes: OK

## Slide 2: Motivation

## Slide 3
from Yale and Swami (2017)
ARMA 17-0644
E dynamic
E static
Static vs dynamic Young’s modulus, E, in rocks

## Slide 4
Elastic media:
Stiffness does not depend on frequency or stress amplitude
Static stiffness = dynamic stiffness

## Slide 5
Rocks are not elastic media
Static stiffness  dynamic stiffness
Main reasons:
Static stiffness is often drained, but dynamic is undrained
Static stiffness depends on stress amplitude (order of MPa), while dynamic is in elastic regime
Stiffness is dependent on stress rate (frequency dispersion)

## Slide 6: Research methodology

## Slide 7: Low frequency apparatus
Ultrasonic P- and
S-wave transducers
Rubber sleeve
Strain gauges
Pore pressure channels
Sample
Force sensor
Piezoelectric
actuator
Internal load
sensor for static
Static force from a
loading frame
Confining
pressure
Axial stress (σax) modulations are applied
Axial () and radial () strains are recorded
Low frequency measurement technique
Measurement | Measured parameters | Frequency | Strain amplitude
Static (undrained) | Young’s modulus, E Poisson’s ratio, | Corresponds to ~0.5 Hz | Up to order of 10-3 m/m
Low frequency | E, | 0.5-150 Hz | ≤10-6 m/m
Ultrasonic | P- and S-wave velocities | 500 kHz | ~10-10 m/m
Measurement | Measured parameters | Frequency | Strain amplitude
Static (undrained) |  | Corresponds to ~0.5 Hz | Up to order of 10-3 m/m
Low frequency |  | 0.5-150 Hz | ≤10-6 m/m
Ultrasonic | P- and S-wave velocities | 500 kHz | ~10-10 m/m

## Slide 8: Linking velocities to engineering parameters
Stiffness matrix for TI medium (e.g. shales)
VP0,VS0 VP90,VS90 VP45
5 independent constants
Ultrasonic
measurement:
Low frequency
measurement:

## Slide 9: Results

## Slide 10: Model by Fjær et al. (2013)
unloading
A
B
z
Non-elastic compliance
dispersion
constants
Non-elastic compliance tends to increase linearly from the start of the unloading;
Semi-empirical model was confirmed in experiments with sandstones and shales
slope
E – local Young's modulus during unloading
Edyn – dynamic (elastic) Young's modulus
– axial stress change
Stress amplitude effect on stiffness Undrained triaxial loading/unloading cycles
Opalinus Clay

## Slide 11: Stress amplitude effect on stiffness Opalinus Clay is highly non-elastic
: 2 MPa
: 1 MPa
: 4 MPa
E [GPa] |  | 
(1MPa) | (2MPa) | (4MPa)
4.3 | 3.3 | 2.3
4.8 | 5.0 | 4.8
Average Stress-strain slope
Zero-strain extrapolation
unloading
Stress amplitude:
unloading
unloading
unloading

## Slide 12: Young's modulus dependance on frequency and stress amplitude
Opalinus Clay
-53%

## Slide 13: Other shales
Field shale 1
Field shale 2
Field shale 2
Field shale 2 demonstrates nearly perfect elastic response

## Slide 14: Velocity dispersion

## Slide 15: Young's modulus dispersion
Field shale 2
Field shale 1
Opalinus Clay

## Slide 16: Conclusions
Static and dynamic stiffness are linked by both stress amplitude (non-elasticity) and stress rate (dispersion) effects
Rocks are non-elastic for strains > 1 strain, both during loading and unloading
With decreasing stress/strain amplitude, the static undrained stiffness approaches the dynamic stiffness of low frequency
In saturated shales, frequency dispersion may strongly affect stiffness
Different mechanisms are responsible for non-elastic effects and dispersion

## Slide 17: Thank you
Acknowledgments:
The Research Council of Norway, AkerBP, DONG Energy, Engie, Maersk and Total through the KPN-project “Shale Rock Physics: Improved seismic monitoring for increased recovery” at SINTEF
NAGRA (National Cooperative for the Disposal of Radioactive Waste)
BP

## Slide 18: Why does the static undrained stiffness differ from the dynamic stiffness?
Strain rate / frequency
 dispersion effects
Stress amplitude
 Activation of non-elastic
processes (focus of this work);
average strain rate of a wave:
f – frequency
ε0 – strain amplitude
18
Dispersion
quasi static
dynamic
Non-elastisity
(Szewczyk et al., 2016)

## Slide 19: Non-elastic process
– friction is suppressing intergranular movement
– sliding is activated
– friction is reactivated after the change in loading direction

## Slide 20: Real experiment Undrained triaxial loading/unloading cycles

## Slide 21: Model by Fjær et al. (2013)
Non-elastic compliance tends to increase linearly from the start of the unloading;
Empirical model was confirmed in experiments with sandstones and shales;
No data available in the vicinity of turning point (small z) due to experimental constrains.
unloading
A
B
z
dispersion
slope
constants
E – local Young's modulus during unloading
Edyn – dynamic (elastic) Young's modulus
– axial stress change
Non-elastic compliance

## Slide 22: Static unloading and low frequency oscillations at various stress amplitudes (0÷0.5 MPa)
Stress path
Compliance:
Water-saturated Castlegate sandstone
Strain rate during unloading is similar to average strain rate of dynamic measurement  dispersion can be neglected
unloading

## Slide 23: Young's modulus dependance on frequency and stress amplitude
1 Mpa
Stress amplitude
2 Mpa
4 Mpa
Opalinus Clay shale
-53%
Average static stiffness
Low-frequency elastic stiffness
Inelasticity
parameter: