## Slide 1: Identifying depleted areas using overburden 4D time shifts
Thomas Røste (Statoil)
ROSE meeting
23.-24. April 2018

## Slide 2: Outline
Why monitor overburden?
Time shifts and geomechanics
Field examples
Summary

## Slide 3
Hydrocarbon
production
Pore-pressure decrease
Reservoir compaction
Stress changes
Overburden displacements
Stretch
Seabed
subsidence
Why monitor overburden
4D seismic time shifts in overburden give information about depleted areas
Independent of reservoir fluid changes

## Slide 4
Reactivated fault
Leakage / pressure build-up
Injector
oozi
Waste Injector
Fractures
Why monitor overburden
4D seismic might capture all effects inducing velocity changes

## Slide 5: 4D Seismic Time Shifts; Snorre
Time Shifts (97-09) @ BCU
A’
A
Published in TLE by
Røste et al. (2015)

## Slide 6: 4D Seismic Time Shifts; Snorre
Balder
BCU
Hordaland
Nordland (Seabed)
SN LL
Depth
(Poor 4D due to TLP)
Time Shifts (97-09) @ BCU
Time Shifts (97-09) @ BCU
A’
A
A’
A
A’
A
Strong overburden 4D time shifts due to geomechanical changes
TS (ms)
2
0
-2
speed-up
slow-down
Published in TLE by
Røste et al. (2015)

## Slide 7
Examples of overburden time shifts
Published in TLE by
Røste et al. (2017)
Slow-
down
Speed-up

## Slide 8: Outline
Why monitor overburden?
Time shifts and geomechanics
Field examples
Summary

## Slide 9
z
v
Baseline
z+Δz
v+Δv
Monitor
4D seismic time shifts capture changes in both thickness (z) and velocity (v)
Røste et al. (2005) and Hatchell et al. (2005) independently assumed:
(1) *
Time shifts and geomechanics
Note! The dilation factor is sometimes referred to as 𝛼.
The relation is
*

## Slide 10
Input:
  Reservoir pressures
  (Eclipse model)
4D geomechanical model:
  Displacements
  Stress changes
  Strain ( )
Output:
  Velocity changes ( )
  Time shifts
Workflow for modelling time shifts
modelled 4D time shifts
Eclipse mod.; ∆P
geomechanical
displacements
Statoil-workflow

## Slide 11: Outline
Why monitor overburden?
Time shifts and geomechanics
Field examples
Summary

## Slide 12: Geomechanical model (97-14)
Max modelled subsidence (97-14) around 0.55 m
Subsidence (m)
0.5
0.4
0.3
0.2
0.1
0.0
0.6
Published in TLE by
Røste and Ke (2017)
Modelled subsidence
A
B
GPS (97-14) ~0.50 m
GPS (97-14) ~0.44 m (GPS)

## Slide 13: Geomechanical model (97-14)
Subsidence (m)
B
A
0.5
0.4
0.3
0.2
0.1
0.0
0.6
Modelled subsidence
Published in TLE by
Røste and Ke (2017)
Gravity Monitoring
(Increasing subsidence)
Max modelled subsidence (97-14) around 0.55 m

## Slide 14: Time Shifts (97-14) @BCU
Modelled
(R=15)
Seismic
Model indicates larger depletion than seismic
Model indicates less depletion than seismic
+3
0
-3
slow-down
speed-up
Published in TLE by
Røste and Ke (2017)

## Slide 15
Seismic
Modelled
(R=15)
Time Shifts (97-09) @BCU
Pressure increase
Pressure depletion
2
0
-2
slow-down
speed-up
Should these faults be sealed?
Pressure depletion
Published in TLE by
Røste and Ke (2017)

## Slide 16: Time Shifts (06-14) @BCU
Seismic
Modelled
(R=15)
1
0
-1
slow-down
speed-up
Published in TLE by
Røste and Ke (2017)
ok match
partly match
Eclipse outdated
mismatch

## Slide 17: inverted - Snorre
Cross-section intersecting an area with large time shifts
Nordland (Seabed)
Hordaland
Rogaland
BCU
TS (97-09) @ BCU
0
20
40
60
80
100
geomech. model
seismic time shifts
S
N
Notes: R-inverted for 97-09

## Slide 18: inverted - Snorre
Nordland (Seabed)
Hordaland
Rogaland
avg ≈ 8
avg ≈ 8
avg ≈ 40
geomech. model
seismic time shifts
S
N
0
20
40
60
80
100
Cross-section intersecting an area with large time shifts
avg ≈ 15
BCU
TS (97-09) @ BCU
Notes: R-inverted for 97-09

## Slide 19: Outline
Why monitor overburden?
Time shifts and geomechanics
Field examples
Summary

## Slide 20: Summary
Overburden geomechanical changes:
  Occur for all fields
  Detected as 4D seismic time shifts
Time shift workflow:
  Useful for updating reservoir model
  Indicates for overburden

## Slide 21: Acknowledgments
Ganpan Ke for fruitful discussions and input to geomechanical models
Colleagues in Statoil and NTNU for discussions, especially:
  Sascha Bussat, Lasse Renli, Martin Landrø, Kenneth Duffaut, Bård Bostrøm, Ola-Petter Munkvold, Øyvind Kvam, Ole K. Søreide, Svend Østmo, Odd Arve Solheim, Jon Lippard, Frank Aanvik, Torill Andersen, Marianne Houbiers, and Vibeke Haugen
The Snorre, Statfjord, and Heidrun partnerships for permission to present this data

## Slide 22: References
Røste, T. and G. Ke, 2017, Overburden 4D time shifts — Indicating undrained areas and fault transmissibility in the reservoir: The Leading Edge.
Røste, T., O.P. Dybvik, and O.K. Søreide, 2015, Overburden 4D time shifts induced by reservoir compaction at Snorre field: The Leading Edge.
Røste, T., A. Stovas, and M. Landrø, 2005, Estimation of layer thickness and velocity changes using 4D prestack seismic data: 67th EAGE, Extended Abstracts, C010.
Hatchell, P.J., R.S. Kawar, and A.A. Savitski, 2005, Integrating 4D seismic, geomechanics and reservoir simulation in the Valhall Oil Field: 67th EAGE, Extended Abstracts, C012.