## Slide 1: Laboratory Measurements as a Tool in Rock Physics Modelling of Uplift
Sondre Torset – Student, NTNU

## Slide 2: Conceptual Model
A dry velocity of 2776m/s is measured at 600 m depth
Granular media models (In this case Hertz-Mindlin) and cementation models (In this case Walderhaug and Dvorkin Nur) can be used to model velocity increase with depth.
Max burial predicted by this result: 2800m
Burial is modelled using Hertz-Mindlin
Cementation is modelled with the models from Walderhaug (1996) and Dvorkin and Nur (1996)
No velocity change during uplift
Cementation assumed to start at 2km depth (70 °C)
Notes: "First, I will give a brief illustration of one method of sandstone modelling throughout the burial history. This is not to say to say that everyone does this, but anyway.
All of these velocities that you will see today are dry. This means that when i say stress I mean effective stress
Let's assume that a (dry) velocity of 2776 is observed at 600m depth.
The idea is then to model compaction with a granular media model (in this case Hertz-Mindlin) and then combine this with cementation models (in this case walderhaug and Dvorkin-Nur)
For those of you familiar with these models, you will see that I have employed some degree of pragmatism to connect Hertz-Mindlin and Dvorkin-Nur, but for this illustration that is not crucial.

## Slide 3: Experimental data
SINTEF conducted experiments with loading and unloading of synthetic sandstones formed under stress.
Clear increase in stress dependence upon unloading
After the cementation the sample seems to retain some stress dependence.
Not a lot of cement
If the experimental data are taken to be a fair representation of the subsurface, the methodology presented previously will over predict velocities, and thus under predict uplift.
See Holt et al. (2014) for a more detailed explanation of the experimental procedure
Notes: Several uncertainty moments to this assumptions of course – how is the cement affected by being subject to loading and subsequent unloading.

## Slide 4: Updated Conceptual Model
The laboratory data suggests a reduced velocity as a result of the uplift
To obtain the observed velocity at 600m, the rock will therefore have to be buried deeper
Uplift is under predicted by 400 meters in this illustration
The actual effect of the uplift is likely to be case dependent
This figure is just meant to serve as an illustration of the concept.
Burial is modelled using Hertz Mindlin
The effect of cementation is modelled with the models from Walderhaug (1996) and Dvorkin and Nur (1996)
The green curve represents the original modelled velocities
The difference between the navy blue and cyan lines is that the cyan line includes deformation modelled by the crack model, right from the onset of uplift.
Cementation assumed to start at 2km depth (70 °C)
P-wave velocity as a function of burial history
The uplift outside the cementation domain is modelled using the crack model in Fjær(2006)

## Slide 5: Anisotropy in the laboratory data
P-wave anisotropy is also preserved after cementation, although it is reduced
Upon uplift the P-wave anisotropy shows a distinctly different behavior compared to loading
See Holt et al. (2014) for a more detailed explanation of the experimental procedure
Can the anisotropy and stress dependence of P-wave velocities be modelled throughout the “burial history” of the synthetic sandstone?
Notes: Several uncertainty moments to this assumptions of course – how is the cement affected by being subject to loading and subsequent unloading.

## Slide 6: Modelling the uplift interval velocities
The crack model presented in Fjær (2006) was tested (among others) to attempt to model the observed velocity changes
This model has three parameters (n, β, η) describing stress sensitivity due to normal stress and shear deformation
The green curves are made by fitting n, β and η using a Levenberg-Marquardt fit of the measured velocities with the measured stress and strains.
It was concluded that the crack model could describe the uplift interval in the experiment.

## Slide 7: Modelling Uplift
Strain is generally not available in the field
Instead of using the experimental strain, an iteration loop for small changes in stress using the generalised Hooke’s law is utilized to estimate input strain in the model
Inputs needed are thus:
  Stress
  Velocity at the start of uplift
  Porosity and Density
Captures the trend at late stages of uplift, but over predicts stress sensitivity at the start of uplift
Since experimental strain is not used, the effect of creep is ignored by the model – continued compactional strain would delay velocity decrease in the crack model.
Measured Radial P-wave velocity
Notes: We start with the crack model because that is the stage most connected to uplift. The implementation is in a for-loop: Assume that small enough variations in stress, the sample follows the generalized Hooke’s law. The axial strain is then given as dsig/C_33 [UNIAXIAL STRAIN ONLY]

## Slide 8: Pragmatic compensation for delayed strain
For these curves the measured velocity is used, but to model the entire burial history requires modelling of the phases prior to uplift

## Slide 9: Pre-cementation loading (Granular media)
Walton (1987) developed relations between stiffness, strain and stress for granular media consisting of infinitely rough or smooth contacts
  Explicit expressions for two strain states states: Uniaxial and Hydrostatic strain
In the experiment, during this phase the loading is conducted with - Neither uniaxial nor hydrostatic strain.
Bandyopadhyay (2009) developed expressions for a biaxial strain scenario, with a basis in Walton (1987) but with some (suspected) errors and a limit on the strain anisotropy
A new model with ideas from Bandyopadhyay (2009) has been made, but correcting the (suspected) mistakes and with no limitation on strain anisotropy

## Slide 10: Post-cementation loading
A model capable of describing both anisotropy and stress dependence in cemented rocks is required.
The patchy cement model described in Avseth et al. (2016) can describe stress sensitivity but not anisotropy.
The model in Avseth et al. (2016) uses an isotropic granular media as the lower bound, but by using an anisotropic granular media instead, the anisotropy can be preserved
The cemented rock stiffness is obtained using the model in Dvorkin and Nur (1996)
The mixing is done using an anisotropic Hashin-Shtrikman formulation found in Parnell and Calvo-Jurado (2015)

## Slide 11: Final result
The three models can then be combined to one continous burial history
All models are wrong, but some are useful – George Box

## Slide 12: Final overview Axial P-wave velocity

## Slide 13: Final overview: Radial P-wave velocity

## Slide 14: Final Overview - Anisotropy

## Slide 15: Limitations and assumptions – could be a pressentation of its own – Quick overview
Lab setup – How translatable are these results to the field case:
  Temperature – higher temperature in the field -> More ductile
  Strain rate – Higher in the lab
  Uniaxial strain during uplift?
Granular media models
  All the assumptions in Walton (1987)
  Mixing of rough and smooth contacts
Cementation models (Anisotropic Patchy Cement)
  The assumption that the rock can be seen as a mixture of cemented (whose stiffness is determined based on Dvorkin and Nur (1996) ) and uncemented grain contacts (whose stiffness is determined by the methodology developed in this work, based on Avseth et al. (2016)).
Crack model
  In the model presented here limited to uniaxial strain.
  Small enough stress and strain  Generalised Hooke’s law in iteration loop with the crack model
  Creep in the experimental data can be compensated.

## Slide 16: Summary
The experiments suggest an increased stress dependence during uplift.
Under uniaxial strain conditions there is also a change in the P-wave anisotropy during simulated uplift compared to burial
These laboratory tests have been used to test a rock physics model that for a set of input parameters models the Axial and Radial P-wave velocities (and thus the P-wave anisotropy) during burial and uplift.
Plethora of limitations and assumptions

## Slide 17: References

## Slide 18: Extra

## Slide 19: Biaxial Walton (rough)
From Walton:
Create expressions for stress and stiffness in terms of 10 integral equations (same procedure as Bandyopadhyay, except the integrals are solved without assumptions)

## Slide 20
Expressions for stress and strain can’t (at least by me) be solved analytically..
But.. Can Newton’s method to solve an equation equal to zero
Very small in the limit of uniaxial compaction is a “limit” effect
Biaxial Walton (rough)
The Newton method is ALWAYS linearly stable (but it may diverge if x0 is sufficiently far from x*) – not the case, know E_r between -0.5 and 0

## Slide 21: Results
The model uses a combination of rough and smooth contacts, as suggested in Bandyopadyhay (2009) ++
In addition, information regarding the grains (coordination number, shear modulus and Poission’s number) is needed
There also exists a parameter that in essence has a similar effect as to make the rough/smooth relationship anisotropic and stress dependent
  Based on the argument that as stress increases the number of rough contacts will increase, and as the loading is not isotropic, this effect will be anisotropic  In essence a fitting parameter for anisotropy
Shear wave velocity for this set of parameters is overpredicted

## Slide 22: Results
APC: Anisotropic Patchy Cement
Radial P-wave velocity stress-sensitivity somewhat overpredicted.
Cement volume in the sample is not actually known exactly (this was not an important parameter for SINTEF), but the amounts are small, and the figures are modelled with a cement volume close to 2%

## Slide 23: Introduction -Motivation
Rock physics modelling of sandstones assuming constant velocity after uplift out of cementation domain
Avseth et al 2016 (Blue is sand)

## Slide 24: Initial shifting
Same n, beta, eta as estimated in specialization project.
Shift (40ms) is somewhat arbitrary to match, but some QC with intermediate (creep gives increase of 50ms)

## Slide 25: New reference point
Same beta and eta as estimated in specialization project. Stress sensitivity (n) has to be altered somewhat to compensate for the change in reference point (n spes = 0.62, n = 0.56

## Slide 26: Motivation
Pre-cementation: Hertz-Mindlin
Cementation
  Assumed to start at 70 °C
  Volume of cement: Walderhaug
  Effect of cement: Dvorkin-Nur
Post-cementation: Crack model
  Parameters somewhat arbitrary, but taken from work in SP
Bytte ut med anisotropy hvis jeg rekker å lage et syntetisk eksempel I tide.

## Slide 27: Previous work
Experimental data (SINTEF):
  Simulated “Burial” and “Uplift” of a synthetic sandstone.
  Constant stress during cementation
  Increase in stress dependence during uplift
  Also not stress independent during burial
  Not isotropic after cementation
  Significant anisotropy change during uplift
If the experimental data are taken to be a fair representation of the subsurface the methodology presented in the previous slide will over predict velocities, and thus under predict uplift.

## Slide 28: Objective M.Sc thesis
Create a model capable of predicting sandstone velocities as a function of rock parameters and stress (burial) history calibrated to the experimental data.
In the field, potentially four stages
  Compaction of granular media prior to cementation
  Continued burial after cementation*
  Uplift during continued cementation
  Uplift after cementation has ceased
In the lab: Cementation prior to burial
* Only considering quartz cementation

## Slide 29
Direct implementation of Crack model – P-wave anisotropy
Anisotropy also suffers from creep, but the trend is captured

## Slide 30: Compensation for creep – Matching the model to the data
3 pragmatic ways to compensate for the creep
  Initial shifting – If left to settle before stress reversal the velocity would increase.
    Upon unloading, the curve obtained from a settled sample compared to an instantly unloaded sample will at some point coincide (Assumption..)
  New reference point – Instead of modelling from the peak stress, the modelling is done from a stress level where there is expected to be no delayed strain in the opposite direction
  Delayed strain directly in the model. Add some strain to the model to simulate the shape of the strain curve observed in the experiment
Notes: Trenger kanskje ikke alle tre metodene