## Slide 1
Gas Field Development
Gas field development involves the optimal selection of well number, well placement, well tubing size, and pipeline characteristics to deliver a specified contract rate (DCQ - daily contract quota) and specified contractual (plateau) period.
The engineering tools required are (a) reservoir material balance(s); (b) well rate equations for reservoir and tubing; and (c) pipeline rate equations. Reservoir simulation is often not necessary, but may be convenient.
Data acquisition is needed early to estimate key parameters in the calculations mentioned in (2). These include core data, log interpretation, geologic mapping, and well testing.
Field gas rate ‘swing’ considerations may be important, accounting for a seasonal variation in production rate demand (maximum in winter).
Compression design may be important during the contractual period, but almost certainly during the decline period of production.
Uncertainty analysis should focus on the parameters which are known to be important and known to be uncertain (IGIP, kh, skin, aquifer strength).
Unit Conversion
Units

## Slide 2
References
Van Dam, Planning of Optimum Production from Gas Fields.
Fetkovich, Multipoint Testing of Gas Wells (backpressure analysis).
Examples
Gas Field Production Forecasting Worked Example
Gas Field Production Forecasting (xls).
Notes