## Slide 1
Gas PVT
The Z-factor gives accurate gas volumetric properties: Bg , g , cg.
Z-factor is particulary important for estimating initial gas in place (IGIP) and gas depletion recovery factors, IGIP = HCPV/Bg.
Z-factor is a function of pressure p, temperature T, and gas composition yi, usually expressed as Z(ppr ,Tpr), according to corresponding states theory, where ppr=p/ppc & Tpr=T/Tpc are pseudoreduced quanties.
Pseudocritical properties ppc and Tpc are functions of gas composition yi (or gas specific gravity g). Special treatment for H2S or CO2.
The accuracy of Z-factors from the Standing-Katz chart should usually be 1-3%.
The Hall-Yarborough BWR equation of state gives an accurate description of the Standing-Katz Z-factor chart for 1<Tr<3 and ppr<25.
Gas viscosities are usually accurate with 5-10%, with increasing expected errors at high pressures and for heavy gases. Typically g=0.02-0.03 cp.
Units
Gas Constant
Unit Conversion

## Slide 2
References
SPE Phase Behavior Monograph, Ch. 3
Examples
Gas Properties
Estimate IGIP and IOIP
SPE Phase Behavior Monograph, App. B
Notes