## Slide 1
The gas rate equation defines the relationship between surface gas rate and pressure drawdown (average reservoir pressure minus bottomhole flowing pressure). This relationship is also called “inflow performance”, reservoir “backpressure curve”, and reservoir “deliverability”.
kh and skin (s+Dq) are the most important variables defining a well’s reservoir deliverability.
For low-rate (low-kh) wells, Dq is usually small (n=1). For high-rate (high-kh) wells, Dq can be significant (0.5<n<1). 
Multirate well tests are used to determine the magnitude of kh, s, and Dq.
Rate behavior in low- to moderate permeability wells may be strongly influenced by transient effects, where the term ln(re/rw) should be replaced by the dimensionless pressure pD(tD).
Combined with the material balance relation, the rate equation can (and should) be used to generate rate-time forecasts.