## Slide 1
Flow Regions. An accurate yet simple model of a gas condensate well undergoing depletion consists of three regions:
Region 1: An inner near-wellbore region where both gas and oil flow simultaneously (at different velocities).
Region 2: A region of condensate buildup where only gas is flowing.
Region 3: A region containing single phase (original) reservoir gas.
For a given producing condition, one, two, or all three regions may exist. These three regions define ‘pseudo steady-state’ flow conditions, meaning that they represent steady-state conditions at a given time but that the conditions change gradually during depletion.