## Slide 1
The volumetric rate equation for a gas condensate well can be expressed in terms of a 2-phase pseudopressure integral. The pseudopressure accounts for ‘condensate blockage’ by including relative permeability krg inside the pressure integral.
Flow to a gas condensate well can be modeled by three regions around the well. Region 1 – the area closest to the well where both oil and gas phases are flowing – dictates productivity loss or ‘condensate blockage’.
The flowing composition is constant in Region 1. The single phase gas entering Region 1 has the same composition as the producing wellbore mixture; this observation leads to the the equation for krg/kro(p) in Region 1.
The pseudopressure integral can be used to model condensate blockage in coarse grid reservoir simulation models; or it can be combined with material balance models to provide a simple model of condensate well performance.
The pseudopressure integral can be extended to include high-velocity and IFT effects on relative permeability -- improvement from high capillary numbers and reduction from ‘inertial’ non-Darcy flow.