## Slide 1
Gas Condensate Reservoirs
A worked example using a simplified simulation model to demonstrate
Recoveries of oil and gas from depletion and from gas recycling in a rich gas condensate reservoir.
Why gas cycling is usually uneconomic (unless there is no route for gas sales), even though it leads to higher oil recoveries.
Comparison of compositional and black oil simulation models.

## Slide 2
Simulation Model
3D model with 9 x 9 x 4 grid – based on 3rd SPE Comparative Solution Project
One injection well and one production well.
Some heterogeneity between layers.
Production well not on edge of model – some of the reservoir will not be swept by injection gas.
Rich gas condensate fluid (180 bbl/MMscf)
Dew point pressure 6765 psi. Initial reservoir pressure 7000 psia.
Injection well
in layers 1 and 2
Production well
in layers 3 and 4
Oil saturations, layer 2, after 5 years

## Slide 3
Development strategies
Depletion
  Maximum gas production rate is 6 MMscf/d
  Limiting BHP = 1500 psi
  Minimum gas rate 0.5 MMscf/d
Gas cycling
  Maximum gas production rate is 6 MMscf/d
  Inject all produced gas for 5 years or 10 years
  Then shut in injection well and produce by depletion.

## Slide 4
Simulation exercise
Run Sensor compositional model for three scenarios
Depletion 
gas recycle for 5 years, then depletion 
gas recycle for 10 years, then depletion 
Look at final recoveries of oil and gas for each scenario. The ‘FIELD SUMMARY’ at the end of the output file gives a table of results which can be copied into an Excel spreadsheet.
Calculate NPV of oil and gas revenues. Assume oil price = $20 /bbl gas price = $3 / MMscf net discount rate = 5%
Repeat calculations for first two scenarios using Sensor Black Oil Model. (Sensor has a very simple way of converting a compositional model to Black Oil.) Compare results of Black Oil and Compositional models.