## Slide 1
Gas Condensate Rate Equation
A worked example to demonstrate the use of the gas condensate rate equation to estimate well productivity, taking account of condensate blockage.
The data will be taken from a Sensor simulation model to allow comparison with simulation results.

## Slide 2: Statement of problem (1)
kh = 1,000 md ft
rw = 0.33 ft
re = 3000 ft
Mechanical skin = 0
Average reservoir pressure = 3965 psia
Wellbore flowing BHP = 1545 psia
Lean gas condensate (PVT properties on next slide), flowing OGR = 26 stb/MMscf
‘Rock’ rel perms, with Corey exponent of 3 (data on slide 4)
Assume oil saturation = 1% outside near-well region
These conditions correspond to this Sensor simulation case after 3 years (1095 days) 10 md, rock rel perms
A well in a lean gas condensate reservoir has with these properties

## Slide 3: Statement of problem (2)
Estimate the maximum gas production rate for the well.
Estimate the condensate blockage skin

## Slide 4: Gas-Oil Relative permeability
Sg | Krg | Krog
0 | 0 | 1
0.04 | 0.0001 | 0.813
0.08 | 0.001 | 0.651
0.12 | 0.0034 | 0.512
0.16 | 0.008 | 0.3944
0.2 | 0.0156 | 0.2963
0.24 | 0.027 | 0.216
0.28 | 0.0429 | 0.1517
0.32 | 0.064 | 0.1016
0.36 | 0.0912 | 0.064
0.4 | 0.125 | 0.037
0.44 | 0.1664 | 0.019
0.48 | 0.2161 | 0.008
0.52 | 0.2747 | 0.0024
0.56 | 0.3431 | 0.0003
0.6 | 0.422 | 0
0.64 | 0.5122 | 0
0.68 | 0.6143 | 0
0.72 | 0.7292 | 0
0.76 | 0.8576 | 0
0.8 | 1 | 0

## Slide 5: PVT properties
PSAT | BO | RS | VISO | rs | BG | VISG
psia | rb/stb | scf/stb | cp | stb/mmcf | rb/scf | cp
750 | 1.1657 | 133.4 | 0.263 | 7.1876 | 0.0047 | 0.014
1000 | 1.2009 | 192.3 | 0.244 | 6.6787 | 0.0037 | 0.0145
1250 | 1.2371 | 254.7 | 0.228 | 6.9745 | 0.0028 | 0.0153
1500 | 1.2741 | 319.8 | 0.214 | 7.7488 | 0.0023 | 0.0158
2000 | 1.3492 | 456.6 | 0.19 | 10.296 | 0.0017 | 0.0171
2500 | 1.4246 | 600 | 0.172 | 13.925 | 0.0014 | 0.0187
3000 | 1.4978 | 746 | 0.158 | 18.498 | 0.0012 | 0.0206
3500 | 1.56 | 881.1 | 0.149 | 23.707 | 0.001 | 0.0228
4000 | 1.5931 | 975 | 0.147 | 28.599 | 0.0009 | 0.0251
4500 | 1.5965 | 1021.4 | 0.149 | 32.167 | 0.0008 | 0.0274
5000 | 1.5982 | 1061.5 | 0.152 | 34.877 | 0.0008 | 0.0295
Dew point pressure of fluid with OGR = 26 stb/Mmscf = 3734 psi

## Slide 6: Step 1. Estimate krg/kro from PVT properties
rp = flowing OGR All other properties from PVT tables
For a fluid with rp = 26 stb/MMscf, dew point pressure = 3734 psi (estimated from PVT table). This is the pressure at the outer edge of Region 1 (P*).
The equation only applies below the dew point pressure.
Above the dew point pressure, kro = 0 and krg/kro = infinity.

## Slide 7: Step 1. Estimate krg/kro from PVT properties
P | krg/kro
1500 | 7.3
2000 | 7.2
2500 | 8.6
3000 | 13.2
3500 | 42.5
3734 | 1000

## Slide 8: Step 2. Estimate krg(P) from krg/kro and rel perm curves
P | krg/kro | krg
1500 | 7.3 | 0.157
2000 | 7.2 | 0.157
2500 | 8.6 | 0.165
3000 | 13.2 | 0.184
3500 | 42.5 | 0.233
3734 | 1000 | 0.96

## Slide 9: Step 3. Calculate the term inside the pseudopressure integral
For field units, the conversion factor c is 0.001127

## Slide 10: Step 3. Calculate the term inside the pseudopressure integral
P (psia) | g (Mscf/stb/cp)
1500 | 4.3
2000 | 5.3
2500 | 6.4
3000 | 7.6
3500 | 10.0
3734 | 41.7
For a lean gas condensate, the second term is very small and can be neglected (< 1% in this example)

## Slide 11: Step 4. Calculate the pseudopressure integral – the area under the Gas mobility vs Pressure curve
This point estimated by extrapolation
The mobility vs pressure curve has a discontinuity at dew point pressure – need to allow for this when evaluating the integral.
Gas mobility g

## Slide 12: Step 4. Calculate the pseudopressure integral
Evaluating the integral by the trapezoid rule gives
= 25,117 psi.Mscf/rb/cp
This gives a gas flow rate of 21.3 MMscf/d.
The gas flow rate from Sensor = 21.5 MMscf/d

## Slide 13: Step 5. Estimate the condensate blockage skin
Recalculate the gas mobility g(P) assuming krg=0.96, kro =0.
The pseudopressure integral is now 90,100 psi.Mscf/rb/cp.
Calculate the skin from
The condensate blockage skin = 21.6. In practice, this is almost certainly too high as it ignores the effect of velocity-dependent rel perms.
Spreadsheet with calculations

## Slide 14: How can we include the effect of velocity dependent rel perms?
Guess the gas production rate.
  this is needed to calculate velocity
For each pressure in the pseudopressure integral
  Estimate the radius by assuming P~ln(radius)
  Estimate the Darcy velocity at this radius
  Estimate the capillary number (will also need IFT as a function of pressure)
  Adjust the krg vs krg/kro relationship using the Fevang-Whitson correlation (Ref 2).
Calculate the pseudopressure integral and the gas production rate.
Repeat if gas production rate is very different from original guess.

## Slide 15: Pseudopressure integral with velocity dependent rel perms
With vel-dep kr
With rock kr
Gas production rate with velocity dependent rel perms is about 31 MMscf/d – a blockage skin of about 12.

## Slide 16
References
Modeling Gas Condensate Well Deliverability
Gas Condensate Relative Permeability for Well Calculations
Engineering Calculations of Gas Condensate Well Productivity
Notes