## Slide 1
Gas Condensate Rate Equation
A worked example to demonstrate the use of the gas condensate rate equation to estimate well productivity, taking account of condensate blockage.
The data will be taken from a Sensor simulation model to allow comparison with simulation results.

## Slide 2: Statement of problem (1)
kh = 1,000 md ft
rw = 0.33 ft
re = 3000 ft
Mechanical skin = 0
Average reservoir pressure = 3965 psia
Wellbore flowing BHP = 1545 psia
Lean gas condensate (PVT properties on next slide), flowing OGR = 26 stb/MMscf
‘Rock’ rel perms, with Corey exponent of 3 (data on slide 4)
Assume oil saturation = 1% outside near-well region
These conditions correspond to this Sensor simulation case after 3 years (1095 days) 10 md, rock rel perms
A well in a lean gas condensate reservoir has with these properties

## Slide 3: Statement of problem (2)
Estimate the maximum gas production rate for the well.
Estimate the condensate blockage skin

## Slide 4: Gas-Oil Relative permeability
Sg | Krg | Krog
0 | 0 | 1
0.04 | 0.0001 | 0.813
0.08 | 0.001 | 0.651
0.12 | 0.0034 | 0.512
0.16 | 0.008 | 0.3944
0.2 | 0.0156 | 0.2963
0.24 | 0.027 | 0.216
0.28 | 0.0429 | 0.1517
0.32 | 0.064 | 0.1016
0.36 | 0.0912 | 0.064
0.4 | 0.125 | 0.037
0.44 | 0.1664 | 0.019
0.48 | 0.2161 | 0.008
0.52 | 0.2747 | 0.0024
0.56 | 0.3431 | 0.0003
0.6 | 0.422 | 0
0.64 | 0.5122 | 0
0.68 | 0.6143 | 0
0.72 | 0.7292 | 0
0.76 | 0.8576 | 0
0.8 | 1 | 0

## Slide 5: PVT properties
PSAT | BO | RS | VISO | rs | BG | VISG
psia | rb/stb | scf/stb | cp | stb/mmcf | rb/scf | cp
750 | 1.1657 | 133.4 | 0.263 | 7.1876 | 0.0047 | 0.014
1000 | 1.2009 | 192.3 | 0.244 | 6.6787 | 0.0037 | 0.0145
1250 | 1.2371 | 254.7 | 0.228 | 6.9745 | 0.0028 | 0.0153
1500 | 1.2741 | 319.8 | 0.214 | 7.7488 | 0.0023 | 0.0158
2000 | 1.3492 | 456.6 | 0.19 | 10.296 | 0.0017 | 0.0171
2500 | 1.4246 | 600 | 0.172 | 13.925 | 0.0014 | 0.0187
3000 | 1.4978 | 746 | 0.158 | 18.498 | 0.0012 | 0.0206
3500 | 1.56 | 881.1 | 0.149 | 23.707 | 0.001 | 0.0228
4000 | 1.5931 | 975 | 0.147 | 28.599 | 0.0009 | 0.0251
4500 | 1.5965 | 1021.4 | 0.149 | 32.167 | 0.0008 | 0.0274
5000 | 1.5982 | 1061.5 | 0.152 | 34.877 | 0.0008 | 0.0295
Dew point pressure of fluid with OGR = 26 stb/Mmscf = 3734 psi