## Slide 1
Gas Condensate
Rate Equation
The volumetric rate equation for a gas condensate well can be expressed in terms of a 2-phase pseudopressure integral. The pseudopressure accounts for ‘condensate blockage’ by including relative permeability krg inside the pressure integral.
Flow to a gas condensate well can be modeled by three regions around the well. Region 1 – the area closest to the well where both oil and gas phases are flowing – dictates productivity loss or ‘condensate blockage’.
The flowing composition is constant in Region 1. The single phase gas entering Region 1 has the same composition as the producing wellbore mixture; this observation leads to the the equation for krg/kro(p) in Region 1.
The pseudopressure integral can be used to model condensate blockage in coarse grid reservoir simulation models; or it can be combined with material balance models to provide a simple model of condensate well performance.
The pseudopressure integral can be extended to include high-velocity and IFT effects on relative permeability -- improvement from high capillary numbers and reduction from ‘inertial’ non-Darcy flow.
Region 1.
Region 2.
Region 3.

## Slide 2
Notes
References
Modeling Gas Condensate Well Deliverability
Gas Condensate Relative Permeability for Well Calculations
Measurement and Correlation of Gas Condensate Relative Permeability
Generalized Pseudopressure Well Treatment In Reservoir Simulation
Engineering Calculations of Gas Condensate Well Productivity
Examples
Worked example for estimating gas production rate
Spreadsheet for calculating krg/kro and krg in Region 1