## Slide 1
Fluid samples from gas condensate wells are needed for two main reasons:
  To provide PVT data for developing a fluid model such as an EOS and/or black-oil tables (“reservoir representative” samples).
  To provide compositional data to define fluids in place, especially surface condensate volume (“in-situ reservoir representative” samples).
Separator samples should almost always be the primary source of samples for gas condensate reservoirs.
Openhole samples (such as MDT) can also be used without complication for wells drilled with water-based muds.
Ideally, samples should be taken while the bottom hole flowing pressure (Pwf) is above the dew point, but this may not be possible in saturated and/or low-permeability reservoirs.
It is still possible to obtain representative samples when (Pwf) is below the dew point. The flow rate should be only as high as needed to lift liquid in the tubing, and large rate changes before sampling should be avoided, particularly rate decreases.
When the flow rate is reduced prior to sampling, the condensate bank ‘unloads’ and gives a sample where the OGR is too high. 
For wells drills with oil-based mud (OBM), it is often possible to back-calculate the reservoir fluid composition by removing OBM components, but this is not straightforward and the contaminated sample may give very different results in PVT experiments.
A series of consistency checks can be used as a Quality Control on reservoir fluid compositions before they are used to model reservoir performance.