## Slide 1
Condensate blockage is the build-up of liquid around the wellbore, reducing the effective gas permeability and lowering well deliverability. 
Condensate saturations in the near-well region can reach 50%, reducing the gas permeability in the near-well region by a factor of 2 to 20.
Condensate blockage is only important when there is a significant pressure drop between the deep reservoir and the well perforations, and when the well is on decline (tubing-pressure limited).
Condensate blockage is more important at low kh. It is likely to be a major issue when kh < ~ 1,000 md-ft. It is unlikely to be significant when kh > ~10,000 md-ft.
The primary relative permeability relationship affecting condensate blockage is krg as a function of krg/kro in the near-well region. Saturation does not enter the calculation.
The impact of condensate blockage can be reduced by an increase in krg at high velocities (capillary numbers, Nc) in the near-well region. Considerable evidence for this effect exists from lab experiments and well tests.