## Slide 1
Modeling Well Performance in Simulation
Use Quality-Controlled PVT data to set up an EoS model of the reservoir. Ensure that gas Z-factors and C7+ content of the gas are matched accurately. Check the predicted depletion recoveries agree with CVD results.
Plot all gas-oil rel perm data in form krg vs krg/kro. Choose data for first estimate of ‘rock’ rel perm curves. If no data available, use Corey functions with ‘crossover’ point of about 0.1. Also plot straight-line (‘miscible’) rel perm curve. 
Calculate krg/kro range for the near-well region in this reservoir. Compare rock and straight-line values in this range, to estimate potential benefit from Capillary Number (Nc) effect. 
Single well, 1D radial, EoS simulation model on fine grid. Include tubing and use THP control. Compare rate-time performance using rock and straight-line rel perm curves to determine if condensate blockage is important. 
If blockage is important, get SCAL data for near-well rel perms. Measure krg as function of krg/kro and Nc. Typically 3 rates for each of 5 values of krg/kro. Cost ~ $100K. Saturation measurements are not really needed. 
Set up fine grid single well model. Include cell-to-cell calculation of Nc effects. When using the E300 model for Nc effects, check that the behavior of krg versus Nc at fixed krg/kro matches experimental data. (If high-rate rel perm data are not available, use the Fevang-Whitson correlation with = 4000, n=0.7), 
Set up a coarse grid, single well model using the Generalized Pseudopressure Model (GPP in Eclipse). Include the Nc effect. Compare results with the fine grid single well model - they should agree, though for lean condensates it may be necessary to use smaller cells in the coarse grid. 
Full field model using coarse grid and GPP model with Nc effects.
Key points to model
Decline in liquid yield with time.
Well deliverability.
  Always include tubing tables.
  Relative permeabilities near well.

## Slide 2
References
Gas Condensate Relative Permeability for Well Calculations
Modeling Gas Condensate Well Deliverability
Calculating Well Deliverability in Gas Condensate Reservoirs.
Examples
Simulation example – Condensate Blockage
Spreadsheet for comparing Eclipse and Fevang-Whitson Nc models
Notes