## Slide 1
Gas Condensate Reservoirs
A worked example using a simplified simulation model to demonstrate
Recoveries of oil and gas from depletion and from gas recycling in a rich gas condensate reservoir.
Why gas cycling is usually uneconomic (unless there is no route for gas sales), even though it leads to higher oil recoveries.
Comparison of compositional and black oil simulation models.

## Slide 2
Simulation Model
3D model with 9 x 9 x 4 grid – based on 3rd SPE Comparative Solution Project
One injection well and one production well.
Some heterogeneity between layers.
Production well not on edge of model – some of the reservoir will not be swept by injection gas.
Rich gas condensate fluid (180 bbl/MMscf)
Dew point pressure 6765 psi. Initial reservoir pressure 7000 psia.
Injection well
in layers 1 and 2
Production well
in layers 3 and 4
Oil saturations, layer 2, after 5 years

## Slide 3
Development strategies
Depletion
  Maximum gas production rate is 6 MMscf/d
  Limiting BHP = 1500 psi
  Minimum gas rate 0.5 MMscf/d
Gas cycling
  Maximum gas production rate is 6 MMscf/d
  Inject all produced gas for 5 years or 10 years
  Then shut in injection well and produce by depletion.

## Slide 4
Simulation exercise
Run Sensor compositional model for three scenarios
Depletion 
gas recycle for 5 years, then depletion 
gas recycle for 10 years, then depletion 
Look at final recoveries of oil and gas for each scenario. The ‘FIELD SUMMARY’ at the end of the output file gives a table of results which can be copied into an Excel spreadsheet.
Calculate NPV of oil and gas revenues. Assume oil price = $20 /bbl gas price = $3 / MMscf net discount rate = 5%
Repeat calculations for first two scenarios using Sensor Black Oil Model. (Sensor has a very simple way of converting a compositional model to Black Oil.) Compare results of Black Oil and Compositional models.

## Slide 5
Simulation results
 | Oil recovery % | Gas recovery % | Field life years
Depletion | 27 | 73 | 10
Gas recycle for 5 years | 55 | 72 | 15
Gas recycle for 10 years | 69 | 70 | 19
Recovery from gas cycling depends on areal and vertical sweep efficiency. In this example, about 40% of the reservoir is swept after 5 years, and about 60% after 10 years.

## Slide 6
Value of oil and gas
production
 | Total revenue $MM | NPV $MM
Depletion | 85 | 68
Gas recycle for 5 years | 109 | 77
Gas recycle for 10 years | 123 | 77
oil price = $20 /bbl gas price = $3 / MMscf net discount rate = 5%
Value of extra revenue from gas cycling is reduced by the delay to gas sales.
Spreadsheet with NPV calculation

## Slide 7
Oil and gas revenues

## Slide 8
Benefits and drawbacks of gas cycling
Gas cycling can improve recovery of liquids, but these benefits are offset by
Delay to gas sales.
Extra CAPEX – more wells, gas injection facilities.
Longer field life.
Gas cycling is mainly used where no gas export facilities are available, or in a few very rich gas condensate fields.

## Slide 9
Comparison of black oil and compositional model results

## Slide 10
Comparison of black oil and compositional model results
Black oil and compositional models give almost identical results for depletion. Published results for full field models confirm this.
For gas cycling, black oil overestimates oil recovery. Final recovery is overestimated by about 6% in this case.
Errors due to black oil model of gas cycling may still be small compared with uncertainties due to reservoir description or PVT properties.
Run times are 3 - 10 times longer for compositional model.

## Slide 11
References
Kenyon & Behie - 3rd SPE Comparative Solution Project SPE 12278
Coats - Simulation of Gas Condensate reservoir Performance SPE 10512
Fevang Whitson – Black Oil vs Compositional Simulation Comparison SPE 63087
El Banbi et al – Black Oil vs Compositional Simulation Comparison for Full Field Gas Condensate Model SPE 58988
Notes