## Slide 1
Liquid saturation in CVD
The CVD ‘liquid dropout curve’ is perhaps the most familiar PVT property of a condensate fluid, but it has little direct impact on reservoir and well performance.
When tuning an EOS model to CVD data, it is much more important to match the gas Z-factor and C7+ fraction in produced gas.
Net revaporization of retrograde condensate starts only at very low pressures (<50 bar). It does not start when the liquid volume starts dropping (e.g. 140 bar above), as this drop is related to solution gas coming out of solution from the retrograde condensate (‘shrinkage’).