## Slide 1
Quality Control Checks on Reservoir Fluid Samples
Plot SG versus MW for C7+ in the separator oil sample. 
Plot log(mole fraction) versus carbon number for SCN fractions in separator oil sample. This should be close to a straight line. Calculate the average molecular weight of the C7+ fraction and compare with the measured value for the C7+ fraction. 
Check K-values for C1 to C6 components at surface separator using Hoffman – Crump –Hocott plot.  Compare linear trend with Standing equation, and if significantly different, then something is wrong with the separator compositions.
Look at how GOR, Psep and Tsep vary with time, and check GOR values used for recombination. Use GOR at time of sampling when recombining separator oil and gas. It is best to use oil rates in separator volumes [m3/d at Tsep, Psep]. Using stock tank oil rates (often reported in well test reports) may introduce an extra uncertainty because of “shrinkage” correction.