## Slide 1: Gas Condensate PVT – What’s Really Important and Why?
Curtis H. Whitson, Øivind Fevang, Tao Yang
PERA
&
NTNU
(Norwegian U. of Science and Technology)
IBC Conference, January 28-29, 1999, London

## Slide 2: Goals
Give a review of the key PVT data dictating recovery and well performance of gas condensate resevoirs.
Understanding the importance of specific PVT data in the context of their importance to specific
mechanisms of recovery and flow behavior.

## Slide 3: Introduction
Gas condensate engineering =
Gas engineering + extra “magic”
Which PVT properties are important …
and why?
Engineering tasks

## Slide 4: Topics of Discussion
PVT Experiments
Initial Fluids in Place and Depletion Recoveries
Condensate Blockage
Gas Cycling Condensate Recoveries
EOS Modeling
Concluding Remarks

## Slide 5: Three Examples
Example 1. A small offshore “satellite” reservoir with high permeability (kh=4,000 md-m), initially undersaturated by 400 bar, and with a test yield of 300 STB/MMscf.
Example 2. A large offshore deep-water reservoir with moderate permeability (kh=1000 md-m), initially saturated or near-saturated (?), large structural relief, and a test yield of 80 STB/MMscf. A single (and very expensive) discovery well has been drilled.
Example 3. An onshore “old” undeveloped gas cap with well-defined initial volume (by production oil wells and pressure history), uncertain initial composition (estimated initial yield of 120 STB/MMscf), partially depleted due to long-term production of underlying oil, and low permeability (kh=300 md-m).

## Slide 6: PVT Priority Lists Vary for Each Reservoir
Different fields require different degrees of accuracy for different PVT properties -- depending on:
  field development strategy
  (depletion vs. gas cycling)
  low or high permeability
  saturated or highly undersaturated
  geography (offshore vs. onshore)
  number of wells available for delineation and development

## Slide 7: PVT Experiments Constant Composition (Mass) Expansion Test
Data
Ps
Z
Vro-Vo/Vt

## Slide 8: PVT Experiments Constant Volume Depletion Test
Data
Ps
yi
Gp/G
Z
Vro

## Slide 9: Initial Fluids in Place (IFIP) and Depletion Recoveries
Gas Z-factor
Compositional (C6+) Variation During Depletion
Compositional Variation with Depth
Dewpoint Pressure
Gas-Oil Contacts

## Slide 10: Gas Z-Factor
Z-factor is the only PVT property which always
needs accurate determination in a gas condensate reservoir.
Initial gas and condensate in place
Gas and condensate recovery as a function of pressure during depletion drive

## Slide 11: Compositional (C7+) Variation During (CVD) Depletion
Forecast the condensate rate profile
Calculate gas and condensate recovery profiles (neglecting water influx/expansion)
Defining Gas Cycling Potential

## Slide 12: Condensate Recoveries from CVD & CCE Data

## Slide 15: Dewpoint Pressure
Dewpoint marks the pressure where:
  Reservoir gas phase
  (= producing wellstream)
  starts becoming leaner
  Incipient condensate phase appears

## Slide 16: Compositional Variation with Depth
Effect of a gradient on IFIPs
Prediction of gas-oil contact using a theoretical gradient model
Effect of compositional gradients on depletion (and cycling) recoveries

## Slide 17: Condensate Blockage Near-Wellbore Steady State Region
krg/kro=(1/Vro – 1)(g/o)
krg = f(krg/kro)
“Pure” PVT
Relative Permeability

## Slide 18: Condensate Blockage Near-Wellbore Steady State Region

## Slide 20: Gas Cycling
Evaluating Gas Cycling Potential using Depletion (CVD & CCE) Data
Evaluating Different Components of Condensate Recovery
  Initial Depletion
  Gas-Gas Miscible
  Vaporization
  Post-Cycling Depletion

## Slide 23: Gas Cycling Ultimate Condensate Recovery
ES = final sweep efficiency at the end of cycling
EV = final efficiency of vaporized retrograde condensate
Cycling Above Dewpoint
Cycling Below Dewpoint

## Slide 24
Gas Cycling Ultimate Condensate Recovery

## Slide 25: “Representative” Samples
“Reservoir Representative”
  Any uncontaminated fluid sample that produces from a reservoir is automatically representative of that reservoir. After all, the sample is produced from the reservoir!
“Insitu Representative”
  A sample representative of the original fluid in place (usually of a limited volume within the reservoir)
  Accuracy of PVT Data ≠ Insitu Representivity of Sample

## Slide 26
EOS Modeling
Molar composition and C7+ Properties
Splitting the plus fraction (3-5 C7+ )
Tuning EOS parameters
“Common” EOS model for multiple reservoir fluids
Reducing number of components (“pseudoizing”)

## Slide 27
Pseudoization Example
EOS22
EOS19
EOS12
EOS10
EOS9
EOS6
EOS4
EOS3

## Slide 28: EOS Modeling
Generating Black-Oil PVT Tables
Extrapolating saturated tables
Non-monotonic saturated oil properties
Consistency between black-oil and EOS models
Handling saturated gas/oil systems
Initializing reservoirs with compositional gradients

## Slide 29: Definition of Black-Oil PVT Properties

## Slide 30: rs/Bgd
“surface oil in place per reservoir gas volume”
(equivalent to CVD y6+)
  The term rs/Bgd is the quantity needed by “geologists” to convert reservoir gas pore volumes to surface oil – a kind of “oil FVF (Bo)” for the reservoir gas phase.
  For compositionally-grading reservoirs with a transition from gas to oil through an undersaturated (critical) state, the term rs/Bgd = 1/Bo exactly at the gas-oil contact.

## Slide 31: Conclusions
For calculation of initial gas and condensate in place the key PVT data are:
Initial Z-factor
Initial C6+ molar content
In terms of black-oil PVT properties, the two "equivalent" PVT quantities are:
Bgd
rs/Bgd

## Slide 32: Conclusions
The constant-composition and constant-volume-depletion tests provide the key data for quantifying recovery of produced gas and condensate during depletion.
Above the dewpoint depletion recoveries of gas and condensate are equal and are given by the variation of Z-factor with pressure.

## Slide 33: Conclusions
For calculation of condensate recovery and varying yield (producing oil-gas ratio) during depletion it is critical to obtain
Accurate measurement of C6+ (rs) variation in the produced gas from a constant volume depletion test.

## Slide 34: Conclusions
even though initial condensate in place can be significantly different for the two initializations
cumulative condensate produced is insensitive to whether the reservoir is initialized with or without a compositional gradient
For near-saturated gas condensate reservoirs producing by pressure depletion:

## Slide 35: Conclusions
Oil viscosity should be measured and modeled accurately to properly model condensate blockage and the resulting reduction in gas deliverability.
The (CCE) oil relative volume Vro has only a "secondary" effect on the modeling of condensate blockage.

## Slide 36: Conclusions
For gas cycling projects above the dewpoint, PVT properties have essentially no effect on condensate recovery because the displacement will always be miscible.
Only the definition of initial condensate in place is important. Gas viscosity has only a minor effect on gas cycling.

## Slide 37: Conclusions
For gas cycling below the dewpoint, the key PVT properties are:
Z-factor variation during depletion
C6+ content in the reservoir gas during depletion
C6+ vaporized from the reservoir condensate into the injection (displacement) gas.