## Slide 1: Volve field Water injection challenges
Image source: equinor.com

## Slide 2: Group 1 Shah RAMS Joe Petroleum Ana IndEcol Sven EE Simon Mech/PM Vladislava ComTech

## Slide 3: Volve basics
Reservoir rock: Hugin formation
Orig. oil in place: 18.7 mill Sm3 (as per factpages.npd.no)
Porosity: High
Permeability: High
Viscosity: Low
Faults: Numerous
Image source: equinor.com

## Slide 4: Production Statistics
Started 2008; shut down 2016
Water injection almost right away (2008)
Early water breakthrough (2009)
By the end of operation oil production had dropped more than 5 times
Orig. recoverable oil: 10.17 mill Sm3 (as per factpages.npd.no) or approx. 54%
Based on data from https://factpages.npd.no/

## Slide 5: Water injection

## Slide 6: Water injection
Water is cheap
Readily available offshore
Water is effective at displacing oil in the reservoir
Can provide external pressure support
  To stay above bubble point pressure
Voidage replacement
Image source: Jahn, F. et.al. (2008). Hydrocarbon exploration and production. 2 ed. Oxford: Elsevier

## Slide 7: Why water injection in Volve
Little to no natural aquifer
  Need for pressure support
Steeply dipping reservoir
Low viscous oil
  Similar viscosity to water

## Slide 8: Volve reservoir challenges

## Slide 9: Volve Faults
Faults introduce total or partial impermeability
Reservoir split into isolated parts
Anticipated more permeable faults
10 producers instead of 3 planned initially
Based on https://data.equinor.com/dataset/Volve, Reservoir Model Eclipse

## Slide 10: Thief zone
“Super permeability” or “speed ” zone
Mainly caused by areal or vertical absolute permeability heterogeneity
Problems: “Reduced oil recovery”
  early water breakthrough causing uneven oil sweep off the reservoirs
  impairs utilization efficiency of injected water
Possible solution: selective plugging
Source: Equinor (Jan 2016), ‘Volve Sim model and HM’ (Powerpoint presentation)

## Slide 11: Reservoir heterogeneity
source:Tarek Ahmed, in Working Guide to Reservoir Rock Properties and Fluid Flow, 2010
Based on https://data.equinor.com/dataset/Volve, Reservoir Model Eclipse

## Slide 12: Water flooding
Late water breakthrough
Factors can affect the shape of flow 1. Gravity 2. Avoid going thief zone 3. mobility ratio (Capillary pressure) 4. Injecting speed
Measurements 1. Open interval should be lower than thief zone. 2. Same water breakthrough time 3. ‘Right’ water
Production wells
Injection wells
Faults
Water flow
Based on https://data.equinor.com/dataset/Volve, Reservoir Model Eclipse

## Slide 13: Water flooding performance
Total water production from 2008 to 2016
Water cut for well P-F-14 and P-F-12
Based on https://data.equinor.com/dataset/Volve, Reservoir Model Eclipse

## Slide 14: Improved recovery

## Slide 15: Suggestions
Planning
More resources on exploration phase
Dedicate more resource to studying faults and their properties
Recovery
Injection of polymer solution
Horizontal wells
Smart Technologies

## Slide 16
Drill or do not drill. There is no try.
“Star Wars: Episode V – The Empire Strikes Back”, 1980